20 June 2014	Reference No. 147613051-001-R-Rev3

John Mitas

Chair of Government Reference Group

Operations General Manager

Department of State Development, Business and Innovation

Level 9, 121 Exhibition Street

Melbourne VIC 3000

RAPID HEALTH ASSESSMENT AND PRELIMINARY REPORT ON MONITORING PROGRAM BASED ON INFORMATION AND DATA AVAILABLE TO 15 JUNE 2014

Dear John

# Summary

This rapid assessment is based on data collected in a two week period.  Samples were collected from shallow soils and tank water and ambient air monitoring was undertaken from one measuring station. This included analysis of 149 samples (58 tank water, 91 surface soils (including 15 road samples)) for antimony and other metals. It also included ambient air monitoring program (PM10, metals, PM2.5).

## The key findings of environmental monitoring:

- Regional soil antimony levels are naturally elevated.  This is the reason antimony is mined in Costerfield.  At present this rapid assessment does not attribute antimony concentrations in urine, soil, water or any other media to any source natural, historical or current.

- Antimony was the key metal measured above guideline levels.  At 33 of 34 residential properties antimony concentrations in tank water were greater than the Australian Drinking Water Guideline. For soil, 13 of 34 residential properties reporting an exceedance of the provisional antimony investigation level.

- Preliminary air monitoring results - indicate low particulate levels (PM10 and PM2.5).  Antimony was measured within these particulates with a maximum ambient air concentration of 0.011 micrograms per cubic metre.

## What do these findings mean for Health?

- Using conservative assumptions the rapid assessment finds that for both adults and children adverse health effects are unlikely.

- Further investigations and a comprehensive risk assessment are warranted to inform ways to reduce antimony exposures to residents.

# Preamble

In order to respond to community concerns regarding antimony exposure in Costerfield, Golder Associates was engaged as an independent expert by a Reference Group of State Government Agencies to conduct an environmental monitoring program and a human health risk assessment.

Recognising the need for a rapid assessment addressing immediate health concerns, this letter report details:

- Rapid health advice to assess potential adverse effects as a consequence of exposure to antimony. This advice is informed by results of a monitoring program comprising:

  - A preliminary sampling and analysis of tank water at residences within Costerfield.  A factual report is provided in Appendix A

  - A preliminary sampling and analysis of surface soil at residences within Costerfield.  A factual report is provided in Appendix B

  - A preliminary air monitoring program at a location within the Costerfield community.  A factual report is provided in Appendix C

  - Data gathering exercise.  Information and data to inform the rapid assessment and planning for the comprehensive risk assessment was provided by:

    - Government Agencies. Regional environmental monitoring data was provided by a number of government agencies.

    - Mandalay Resources.  Data on the mining operations, and environmental monitoring was provided by the company.

The monitoring program was developed to meet the objectives of the Reference Group Scope of Works. It was conducted in a manner consistent with relevant Australian Sampling and Analysis guidelines.  Surface soil and water analytical results were reported and carried out in National Association of Testing Authorities (NATA) accredited laboratories using NATA endorsed analytical methods.  Air quality sampling and analysis was conducted in accordance with Golder’s NATA Laboratory Accreditation (Number 1910).  Quality assurance procedures were undertaken.

Further comprehensive risk assessment will incorporate the results of additional testing and data analysis.

# Key Points available on 16 June 2014:

- Mandalay Resource process antimony ore in the form of Stibnite.  This is converted from rock to a fine powder before being further concentrated within an operating plant.

- Stibnite (antimony trisulphide, Sb2S3, CAS Number 1345-04-6) is a black crystalline solid and is sparsely soluble in water.   It is a trivalent species of antimony (Grund 2012).

- Stibnite (antimony trisulphide) is categorised by the European Chemicals Agency Database on Registered Substances as “Non Hazardous” (ECHA 2014).  Consistent with this, the International Agency for Research on Cancer (IARC) evaluation on the evidence for the carcinogenicity of Stibnite concluded (IARC 1989) that there is insufficient evidence to categorise Stibnite as a carcinogen (Group 3).  Antimony and other antimony compounds are hazardous substances.  In particular antimony trioxide has been evaluated by IARC as Group 2B possibly carcinogenic to humans.  This evaluation was based on evidence in experimental animals that antimony trioxide caused lung tumours following high exposures to antimony dust (IARC 1989).

- The skin is a good barrier to metal compounds.  There is no evidence that antimony is absorbed through skin at an appreciable rate.  Dermal absorption of antimony following bathing in tank water (for example) is therefore expected to be a minor pathway for exposure.

- Antimony exists in a number of forms depending on environmental conditions, particularly pH and oxygen content.  Typically antimony is present as a pentavalent or trivalent oxide form (Takaoka 2005).

- The Victorian Department of Health has produced a fact sheet on the toxicity of antimony.  This is provided in Appendix D of this report as a reference guide.

- For the Costerfield monitoring program, 149 samples (58 tank water, 91 surface soils) were analysed for a range of metals including antimony and another seven metals.  Ambient air monitoring involved PM10 samples, analysed for 12 metals, including antimony, PM2.5 samples, deposited dust samples, analysed for metals and insoluble solids and continuous PM10 measured using an indicative instrument.   The surface soil samples included 15 road dust samples.

- The monitoring program identified antimony as the key metal measured above guideline levels.

- Elevated levels of antimony were widespread in tank water and soil.  Of the 58 tank water samples, 52 reported antimony concentrations greater than the Australian Drinking Water Guideline (3 micrograms per litre).  For soil, twenty-two of 91 surface samples reported antimony at concentrations greater than the preliminary health investigation level (200 milligrams per kilogram).

- The form of antimony present from tank water is a soluble form.  The total and filtered antimony concentrations in tank water were comparable.  It should be noted that antimony concentrations of samples taken from inside the tanks were comparable to concentrations from the tap.

- Interim air monitoring results collected to date demonstrated low particulate levels (PM10 and PM2.5).  Antimony was measured within the PM10 samples with a maximum ambient air concentration of 0.011 micrograms per normal cubic metre.

- Survey data that pre-dates current mining operations indicates high regional soil concentrations of antimony in the Costerfield region.  Given the geological / mineralogy of the region, together with historical mining activities since the 1860’s, the elevated antimony soil concentrations are not unexpected.

- A preliminary and limited statistical assessment of soil data (collected within the Study Area, as well as regional data within a 5 kilometre radius), indicated that the Study Area antimony concentrations in soil are higher than the regional values (Arne 2009).  Whether this is due to current mining operations or historical mining has not been determined as part of this rapid health assessment.

- A preliminary review of Mandalay dust deposition gauge data indicated that nuisance standards were exceeded on frequent occasions particularly in the areas with prevailing wind from the processing operations (west and north).

- The health significance of the measured elevated antimony in tank water and surface soil is considered in this rapid health assessment.

- A comprehensive risk assessment informed by additional data will assess exposure pathways and distinguish potential sources of contamination in more detail.

.

# What does a Rapid Health Assessment entail?

Rapid Health Assessment is an objective and scientific approach based on limited data to assess potential adverse effects as a consequence of exposure. This rapid assessment uses information collected within a two week period and risk calculations to consider health issues to Costerfield residents.

The rapid assessment makes a number of conservative assumptions to err on the side of caution.  It also assesses two scenarios:

Scenario 1:  Residents are exposed to antimony via inhalation of ambient particulates, incidental ingestion of soil and use tank water as their primary drinking water source on a daily basis.

Scenario 2:  Residents are exposed to antimony via inhalation of ambient particulates, incidental ingestion of soil to soil and ambient air.  Residents do not use tank water as their primary drinking water.

The results are presented for both scenarios and for each property (de-identified for privacy reasons) for:

- Adults weighing 100 kilograms (frequently observed weight)

- Adults weighing 70 kilograms (approximate average weight of Australians)

- Children weighing 30 kilograms (approximately 5 years of age)

- Children weighing 15 kilograms (i.e.2 year old toddler)

- Children weighing 10 kilograms (i.e. 1 year old infant)

# What are the key steps in the Rapid Assessment?

There are three key steps:

Step 1 – Estimate Intake of antimony

Step 2 – Compare Estimated Intake to a Tolerable Daily Intake of antimony

Step 3 – Assess Margin between the Estimated Intake and Intakes suspected or known to cause adverse health effects

## Step 1 – Estimate Intake (Intake based on rapid measurements in soil, water, air)

The estimated intake is the amount of antimony taken into the body by ingestion and inhalation.  It is expressed either as micrograms of antimony per person per day or micrograms of antimony per kilogram body-weight per day. The estimate is based on the maximum concentrations of antimony measured in drinking water, soil and ambient air.  In addition the estimate uses conservative assumptions about consumption rates.  It does not include averaging terms based on exposure frequency (part of the day, number of days per year, number of years).  That is, the estimated intake assumes that people are exposed to the maximum measured concentration, assuming a 24 hour exposure.  Such an estimate is intended to err of the side of caution.

## Step 2 – Compare Estimated Intake to a ‘Tolerable daily intake’

The tolerable daily intake (TDI) is defined as the amount of daily intake of a substance that can occur over a lifetime without appreciable lifetime health risk. It is typically expressed in units of micrograms per kilogram body-weight per day (WHO 1994).

The World Health Organisation reviewed the toxicology of antimony in 2003 and determined that a tolerable daily intake for humans over a lifetime is 6 µg/kg bw (6 micrograms per kilogram body-weight).  This translates to:

- 600 micrograms antimony per day for a 100 kilogram man or woman

- 420 micrograms antimony per day for a 70 kilogram man or woman

- 180 micrograms antimony per day for a 30 kilogram child (5-7 year old)

- 90 micrograms antimony per day for a 15 kilogram child (approximately 18 -36 month old)

- 60 micrograms antimony per day for a 10 kilogram child (approximately 1 year old)

The tolerable daily intake is derived to err on the side of caution.  It is derived:

- within an objective scientific process called risk assessment to enable decisions concerning the protection of human health.  That is, a tolerable daily intake is not the boundary of when adverse health effects are likely to occur.

- in a manner that provides protection of human health following average daily exposure in the ambient environment for a lifetime.

- to be protective of identified and proven sensitive subpopulations within the general population.

- in a clear and transparent fashion following a comprehensive review and evaluation of available information on the biological effects of a substance.

## Step 3 – Assess Margin between Intakes at which health effects are known and the Estimated Intake

The main intake pathway of antimony for this assessment was oral exposure via drinking water and incidental ingestion of soil.  A number of reviews on the toxicology of antimony have been published and document effects in humans and in animal studies.  From these reviews the following can be stated:

- Single oral doses of antimony at concentrations of 30,000 to 60,000 micrograms cause vomiting and other intestinal symptoms such as nausea and abdominal pain.  These doses are equivalent to 430 to 850 micrograms of antimony per kilogram bodyweight for a 70 kilogram adult.  Antimony-based medicine (tartar emetic) for inducing vomiting was historically used in medicine.

- In humans, antimony is used in medicine to treat severe parasite related diseases (Leishmaniosis).  The World Health Organisation recommends a schedule of injections in the muscle or veins of 20,000 micrograms pentavalent antimony per kilogram body-weight per day for 10–20 days.  This is based on a maximal daily dose of 850,000 micrograms antimony per day (Berman 1988, WHO 1984).  Side effects have been noted.  Antimony can cause cardiac toxicity when given by injection at doses higher than 20,000 micrograms per kilogram pentavalent antimony.

- The World Health Organisation in its recent review of the toxicology of antimony following oral administration decided that the lowest no observed adverse effect level was 6000 micrograms per kilogram body-weight per day.  At higher doses (45,000 micrograms per kilogram body-weight) marked but reversible loss of body-weight gain occurred, together with slight changes to liver and spleen, probably related and in conjunction with distinctly reduced food and water intake at this dose.

In order to err on the side of caution the no observed effect level selected by the World Health Organisation was used to compare to the estimated intakes from the Costerfield monitoring program.

# Results of Step 2: Do Estimates of Exposure Exceed the Tolerable daily intake?

Results for both Scenario 1 (soil, tank water and air exposure) and Scenario 2 (soil and air but no tank water exposure) for each Residence are displayed in Figure 1 and Figure 2 respectively.  The results show:

- For adults the estimated intakes of antimony are below (1.6 to 250 times less than) the tolerable daily intake.

- For a 1 year old child (10 kg) the estimated intakes of antimony in 9 of the 34 residences in Scenario 1 (tank water used as a drinking water source) is above (up to 5 times greater than) the tolerable daily intake for a 10 kg child.

- For a 1 year old child (10 kg) the estimated intakes of antimony in 7 of the 34 residences in Scenario 2 (tank water not used as a drinking water source) is above (close to 5 times greater than) the tolerable daily intake for a 10 kg child.

- For 2 year old children (15 kg) the estimated intakes of antimony in six of the 34 residences in Scenario 1 (tank water used as a drinking water source) is above (up to 3.5 times greater than)  the tolerable daily intake for a 15 kg child.

- For 2 year old children (15 kg) the estimated intakes of antimony in three of the 34 residences in Scenario 2 (tank water not used as a drinking water source) is above (close to 3.5 times greater than)  the tolerable daily intake for a 15 kg child.

- For 5 year old children (30 kg), the estimated intakes of antimony in three of the 34 residences in Scenario 2 (tank water not used as drinking water) is above (up to 3.3 times greater than) the tolerable daily intake for a 30 kg child.

- For 5 year old children (30 kg), the estimated intakes of antimony in two of the 34 residences in Scenario 2 (tank water not used as drinking water) is above (3 times greater than) the tolerable daily intake for a 30 kg child.

## Conclusions for Step 2

The results do not mean people are at risk of adverse health effects.   This is addressed in Step 3.

The results do mean a more thorough understanding of the environmental levels of antimony and potential exposure routes is necessary.  It also means measures may be necessary to reduce intake in children.  It does not mean children will experience adverse health effects (refer to Step 3).

Figure 1: Scenario 1: Comparison of Estimated Daily Intake to Tolerable Daily Intake (Estimated intake assumes ingestion of soil, water and inhalation of particulates in air).

1A: Adults. Intakes expressed in micrograms per day (µg/day) compared to the tolerable daily intake (TDI) for an adult (male or female) weighing 70 or 100 kilograms (kg)

Summary for Adults:

- Adult intakes are lower than the TDI at all locations

- Intake estimates assume ingestion of 50 mg of soil and 2 litres of water per day

1B: Children.  Intakes expressed in micrograms per day compared to the tolerable daily intake (TDI) for 1 year, 2 year and 5 year old children

Notes: TDI = Safe average intake or tolerable daily intake; µg/day = micrograms of antimony per day; kg = kilograms; ID = individual identifier

Summary for Children:

- For 1 year olds, intakes are greater than the TDI at 9 locations.

- Intake estimates assume ingestion of 100 mg of soil and 1 litre of water per day

Scenario 1 intakes are based on intakes from tank water (drinking water), soil (ingesting soil) and air (inhaling particles). Soil and water contributions differ between properties depending on the soil and water concentration measured.  For children (all ages assessed) tank water contributes between 3.3% and 96.5% of intake.

Figure 2:Scenario 2 Comparison of Estimated Daily Intake to Tolerable Daily Intake (Estimated intake assumes ingestion of soil, and inhalation of particulates in air).

2A: Adults. Intakes expressed in micrograms per day (µg/day) compared to the tolerable daily intake (TDI) for an adult (male or female) weighing 70 or 100 kilograms (kg)

Notes: TDI = Safe average intake or tolerable daily intake;

µg/day = micrograms of antimony per day; kg = kilograms; ID = individual identifier

Summary for Adults:

- Scenario 2 assumes tank water is not used for drinking purposes.

- Adult intakes are lower than the TDI at all locations

- Intake estimates assume ingestion of 50 mg of soil.

2B: Children.  Intakes expressed in micrograms per day compared to the tolerable daily intake (TDI) for 1 year, 2 year and 5 year old children

Notes: TDI = Safe average intake or tolerable daily intake; µg/day = micrograms of antimony per day; kg = kilograms; ID = individual identifier

Scenario 2 Summary for Children:

- For 1 year olds, intakes are greater than the TDI at 7 locations.

- Intake estimates assume ingestion of 100 mg of soil and no tank water is ingested.

Scenario 2 allows people to assess the contribution of soil because practically all of the intake is due to soil.  This is because Scenario 2 assumes tank water is not used for drinking purposes.  All intakes are lower than those for Scenario 1.  However at some properties (1, 11, 32, 34), Scenario 2 shows that soil is an important contributor to exposure.

# Results of Step 3 - Are Adverse Effects Likely in Children?

The likelihood of adverse effects occurring due to chemical intake is judged by the margin between the adverse effect level and the estimated intake.  This is called the margin of exposure.  Given that the estimated intakes of antimony for adults were all below the tolerable daily intake (i.e. a minimum margin of 1000 fold) this assessment step was only performed for children. In this instance a margin of less than 100 is interpreted as an immediate concern for adverse health effects.

The margins of exposures for children were found to be greater than 100.  The margins of exposures for Scenario 1 (tank water used as drinking water) were found to range between 196 and 99 000 fold.  The margins of exposures for Scenario 2 (tank water not used as drinking water) were found to range between 202 and 222 000.  Therefore adverse effects are not expected to occur at the estimated intakes.

Figure 3 provides a comparison of the child margins of exposure for both Scenario 1 and 2.

Figure 3: Results of “Step 3” – Margin of Exposure

Notes: 
* Units = µg/ kg bw/day
 µg/ kg bw/day = micrograms per kilogram body weight per day; kg = kilograms
TDI = Safe average intake or tolerable daily intake
A margin of less than 100 indicates potential for  adverse health effects

# In Summary

Based on the results of the monitoring program, the rapid assessment indicates that health effects are not expected in residents from antimony exposure in Costerfield.  Further assessment of exposure pathways and ambient air levels are necessary to consider the plausibility of other exposure routes and confirm the current findings.

In the meantime residents should take steps to reduce their potential exposure to antimony from environmental sources.

## What do the results of this Rapid Assessment mean for urine levels?

Antimony levels in urine are a measure of the levels of antimony in the body.  If antimony levels in the environment are elevated then the amount of antimony taken into the body will be elevated and the levels in urine will also be elevated.

Elevated antimony concentrations in urine are a marker of exposure and not human health impact.  Urine levels can be elevated and still not result in human health effects.

## Conservative Aspects of this Rapid Assessment

The Costerfield area is naturally high in antimony. That is why there is a mine in Costerfield.  Mining activities over 150 years are likely to have added antimony to surface soils.  The rapid assessment does not consider the origin of the elevated soil concentrations of antimony.  These could be of natural origin, historical mining related or due to current mining operations.

The rapid assessment assumes:

- Children eat 100 milligrams of soil each day while they play at a residential property.  Children play in the area where the maximum soil concentration was measured.  In addition no averaging period was assigned to this exposure.  For instance a child may only play outside on a proportion of the number of days per year and live at the residences for certain number of years.  The exposure frequency and duration have not been considered.

- People (both adults and children) drink tank water as their sole source of drinking water (for Scenario 1).  Once again, no averaging period was assigned to the exposure.

## Data Gaps

- The levels and sources of antimony in local air are not well understood.

- Antimony in ambient air (and therefore tank water) may be elevated due to elevated levels in soil (a major contributor to the elevated intakes in Costerfield).  Further investigation is needed to characterise ambient soil background concentrations not effected by mining occurrence and with depth.

- There is a need to consider other sources of antimony exposure, such as diet.

- The rapid assessment does not consider impacts on stock, pets or wildlife.

- Some of the toxicological aspects of antimony need further assessment.  For instance:

  - The current assessment assumes 70% of the antimony in soil is available for uptake by the human body.  This could be considerably different (likely to be a lower value) in practice.

  - The latest revision of the Australian Drinking Water Guideline for Antimony (3 micrograms per litre) was in 1996.  In 2003 the World Health Organisation based on a review of more recent toxicology studies set a drinking water guideline value at 20 micrograms per litre.

## Strategies to Reduce Exposure

Most residences within Costerfield are likely to have low exposures.  There are a small number of residences that if children were present every day there would be a need to reduce exposure levels.  Measures to reduce exposure could include:

- Using drinking water that complies with the drinking water standard

- reducing indoor dust

- reducing soil exposures (e.g. replace soil in play areas and garden beds).

References

Arne D.C., 2009. Compilation of open-file surface geochemical data from Bendigo 1:250 000 map sheet and adjacent areas, Victoria. GeoScience Victoria Gold Undercover Report 20. Department of Primary Industries.

enHealth (2012). Australian Exposure Factor Guidance. enHealth Council, Department of Health and Ageing, Canberra.

Berman J., D. (1988). Chemotherapy for Leishmaniasis. Biochemical Mechanisms, Clinical Efficacy, and Future Strategies.  Reviews of Infectious Diseases, Volume 10(3) (May-Jun 1988) p560-586.

ECHA (2014) Registered Substances Database Search for Stibnite. Accessed 12 June 2014. http://echa.europa.eu/information-on-chemicals/registered-substances

Grund, S., C., Hanusch, K., Breunig, H., J., Wolf, H., U. (2012).  Antimony and Antimony Compounds.  In ‘Ullmans Encyclopedia of Industrial Chemistry’ Published by Wiley-VCH Verlag GmbH & Co. KGaA, Weinheim DOI: 10.1002/14356007.a03_055.pub2.

IARC (1989). Antimony trioxide and Antimony trisulfide.  International Agency for Research on Cancer (IARC) Monographs, VOL.: 47 (1989) (p. 291) Lyon France.

NHMRC (2011). Australian Drinking Water Guidelines EH52 - Updated December 2013. National Health and Medical Research Council.

Takaoka, M., Fukutani, S., et al. (2005). Determination of Chemical Form of Antimony in Contaminated Soil around a Smelter using –ray Absorption Fine Structure.  Analytical Sciences July 205, v21, p769-772.

World Health Organization (WHO) (1994). Assessing human health risks of chemicals: Derivation of guidance values for health-based exposure limits. Environmental Health Criteria 170. IPCS/ WHO. Geneva: WHO.

WHO (2010). Control of Leishmaniases. Report of a meeting of the WHO Expert Committee on the Control of Leishmaniases, Geneva, 22–26 March 2010

WHO (2003). Antimony in Drinking-water. Background document for development of WHO Guidelines for Drinking-water Quality. World Health Organisation. WHO/SDE/WSH/03.04/74

WHO (2011). Guidelines for drinking-water quality, fourth edition. World Health Organization.

Yours sincerely

GOLDER ASSOCIATES PTY LTD

John Frangos	Ian Kluckow

Principal Toxicologist	Principal

JF:NF/CB:IK/dl

Attachments: Limitations

Appendix A: Tank Water Monitoring – Factual Report

Appendix B: Soil Sampling - Factual Report

Appendix C: Laboratory Report

Appendix D: Copy of Department of Health Community Fact Sheet for Antimony May 2014

j:\env\2014\147613051 - costerfield\correspondence out\147613051-001-r\147613051-001-r-rev1\147613051-001-r-rev2.docx

# LIMITATIONS

This Document has been provided by Golder Associates Pty Ltd (“Golder”)

subject to the following limitations:

This  Document  has  been  prepared  for  the particular  purpose  outlined  in Golder’s  proposal  and  no  responsibility  is  accepted  for  the  use  of  this Document, in whole or in part, in other contexts or for any other purpose.

The scope and the period of Golder’s Services are as described in Golder’s proposal, and are subject to restrictions and limitations.  Golder did not perform a complete assessment of all possible conditions or circumstances that may exist at the site referenced in the Document.  If a service is not expressly indicated, do not assume it has been provided.  If a matter is not addressed, do not assume that any determination has been made by Golder in regards to it.

Conditions may exist which were undetectable given the limited nature of the enquiry Golder was retained to undertake with respect to the site.  Variations in conditions may occur between investigatory locations, and there may be special conditions pertaining to the site which have not been revealed by the investigation and which have not therefore been taken into account in the Document. Accordingly, additional studies and actions may be required.

In addition, it is recognised that the passage of time affects the information and assessment provided in this Document.  Golder’s opinions are based upon information that existed at the time of the production of the Document.   It is understood that the Services provided allowed Golder to form no more than an opinion of the actual conditions of the site at the time the site was visited and cannot be used to assess the effect of any subsequent changes in the quality of the site, or its surroundings, or any laws or regulations.

Any assessments made in this Document are based on the conditions indicated from  published  sources  and  the  investigation  described.  No  warranty  is included, either express or  implied, that  the actual conditions will conform exactly to the assessments contained in this Document.

Where data supplied by the client or other external sources, including previous site  investigation  data,  have  been  used,  it  has  been  assumed  that  the information is correct unless otherwise stated. No responsibility is accepted by Golder for incomplete or inaccurate data supplied by others.

Golder may have retained subconsultants affiliated with Golder to provide Services for the benefit of Golder.  To the maximum extent allowed by law, the Client acknowledges and agrees it will not have any direct legal recourse to, and waives any claim, demand, or cause of action against, Golder’s affiliated companies, and their employees, officers and directors.

This Document is provided for sole use by the Client and is confidential to it and its professional advisers. No responsibility whatsoever for the contents of this Document will be accepted to any person other than the Client.  Any use which a third party makes of this Document, or any reliance on or decisions to be made based on it, is the responsibility of such third parties.  Golder accepts no responsibility for damages, if any, suffered by any third party as a result of decisions made or actions based on this Document.

GOLDER ASSOCIATES  PTY LTD	GAP Form No.  LEG 04  RL 1

APPENDIX A

Tank Water Monitoring – Factual Report

17 June 2014

Report No. 147613051-001-R-Rev1

16 June 2014	Reference No. 147613051-003-L-Rev0

Mr John Mitas

Chair of Government Reference Group

Operations General Manager

Department of State Development, Business and Innovation

Level 9, 121 Exhibition Street

Melbourne, 3000

Victoria

TANK WATER MONITORING FACTUAL REPORT, COSTERFIELD

Dear John

# 1.0	INTRODUCTION

Golder Associates Pty Ltd (Golder) was commissioned by the Department of State Development, Business and Innovation (DSDBI) to undertake a preliminary assessment of drinking water sourced from rainwater tanks at residential properties located in Costerfield, Victoria (the assessment area).

# 2.0	OBJECTIVE AND SCOPE OF WORKS

The objective of this study was to undertake a preliminary assessment of antimony levels in drinking water supplied by domestic rainwater tanks within the assessment area. The scope of works comprised:

- Collection of 58 water samples at 33 properties within the assessment area and 1 property outside of Costerfield.  Water samples were collected at each premise from accessible sampling points including;

  - kitchen taps

  - taps on rainwater tanks &/or

  - outdoor taps

- Anecdotal information indicates that some of the rainwater tanks are topped up by an alternative water source.

- The preliminary assessment was conducted in a manner consistent with relevant  water sampling standards:

  - Australian/New Zealand Standard 5667.1 (1998) Water Quality – Sampling Part 1: Guidance on the design of sampling programs, sampling techniques and the preservation and handling of samples.

  - Australian/New Zealand Standard 5667.5 (1998) Water Quality – Sampling Part 5: Guidance on sampling of drinking water and water used for food and beverage processing.

- Laboratory analysis of samples for total dissolved solids, pH, sulphate, total and dissolved metals (including antimony, arsenic, cadmium, copper, iron, lead, nickel and zinc).

- The laboratory results were screened against national and international drinking water guidelines:

Golder Associates Pty Ltd

Building 7, Botanicca Corporate Park, 570 – 588 Swan Street, Richmond, Victoria 3121, Australia (PO Box 6079, Hawthorn West VIC 3122) Tel: +61 3 8862 3500  Fax: +61 3 8862 3501  www.golder.com

Golder Associates: Operations in Africa, Asia, Australasia, Europe, North America and South America

A.B.N. 64 006 107 857

Golder, Golder Associates and the GA globe design are trademarks of Golder Associates Corporation.

	National Water Quality Management Strategy Australian Drinking Water Guidelines 6 Version 2.0,

2011 (ADWG, 2011).

	World Health Organisation Guidelines for Drinking Water Quality, 2011 (WHO 2011).

Further detail on the methodology and drinking water guidelines adopted is presented in Attachment A.

# 3.0	DATA QUALITY ASSURANCE AND QUALITY CONTROL

The field and laboratory procedures implemented for quality assurance/quality control (QA/QC) along with a discussion of the QA/QC results are presented in Attachment B.

Quality control samples collected as part of the sampling program included collection of field duplicates and field splits at a rate of at least 5 per cent, collection of rinsate blanks and container blanks. The laboratories implemented a Quality Control (QC) program including analysis of internal spikes, duplicates and method blanks.

The data quality objective for the program was a completeness target of 95%. An overall completeness of 97.8% was achieved, satisfying the overall data quality objective for the program. Golder considers that the overall data quality generated during the assessment is of sufficient quality upon which to base decisions for this assessment.

# 4.0	RESULTS

A total of 58 samples were collected and submitted to ALS Environmental Laboratories for analytical testing. The analytical results have been tabulated and screened against relevant drinking water guidelines. The results for all chemicals tested for are presented in Table A attached to this report.

A summary of antimony results are presented in Table 1 below.

Table 1: Summary of antimony analytical results

| Laboratory analysis | Range of reported results | Number of samples analysed | Drinking water guidelines | Number of samples exceeding drinking water guidelines |
| --- | --- | --- | --- | --- |
| Total antimony | <0.001 - 0.106 mg/L | 58 | WHO 2011 (0.020 mg/L) | 17 |
|  |  |  | ADWG 2011 (0.003 mg/L) | 53 |
| Dissolved antimony | <0.001 - 0.110 mg/L |  | WHO 2011 (0.020 mg/L) | 19 |
|  |  |  | ADWG 2011 (0.003 mg/L) | 52 |

WHO 2011 – World Health Organisation; ADWG 2011 - Australian Drinking Water Guidelines.

The preliminary assessment of antimony results for water sourced from domestic rainwater tanks within the assessment area found:

- Antimony was generally detected above the adopted Australian drinking water guideline (ADWG 2011).

- Approximately one third of the antimony results are above the adopted World Health Organisation (WHO 2011) drinking water guideline.

- Reported total and dissolved concentrations are comparable indicating that antimony is predominantly present in a dissolved form.

- Exceedances of the Australian drinking water guideline were reported for the 33 residential properties sampled within the Costerfield area. The single property sampled outside the Costerfield area did not report antimony levels above the Australian drinking water guideline.

# 5.0	LIMITATIONS

Your attention is drawn to the document - “Limitations”, which is included in Attachment C of this letter. The statements presented in this document are intended to advise you of what your realistic expectations of this report should be. The document is not intended to reduce the level of responsibility accepted by Golder, but rather to ensure that all parties who may rely on this report are aware of the responsibilities each assumes in so doing.

# 6.0	CLOSURE

If you have any questions please do not hesitate to contact the undersigned. Yours sincerely

GOLDER ASSOCIATES PTY LTD

Nic Foot	Christian Wallis

Senior Environmental Engineer	Principal Environmental Scientist

SH:NF/CJW/nw

CC:	The Government Reference Group

Attachments: Table A – Analytical Results

Attachment A – Sampling Methodology

Attachment B – Data Quality Assurance and Quality Control

Attachment C – Limitations

\\golder.gds\gap\melbourne\jobs\env\2014\147613051 - costerfield\correspondence out\147613051-003-l_tank water factual report\147613051-003-l-rev0_ready for pdf\01_147613051-003-l-rev0.docx

Table A: Analytical Results	Water Tank Monitoring

Costerfield

147613051

Heavy Metals

Sample Quality Parameters

mg/L	mg/L	 mg/L	 mg/L	 mg/L	 mg/L	mg/L      mg/L      mg/L     mg/L	 mg/L	 mg/L	 mg/L	 mg/L	 mg/L	mg/L	pH_Units	pH_Units	mg/L	mg/L LOR	0.001      0.001	0.001	0.001	0.0001	0.0001      0.001     0.001      0.05	0.05	0.001	0.001	0.001	0.001	0.005      0.005			0.01	   10	   1

ADWG 2011 Aesthetic 	1	1	0.3	0.3	3	3	6.5-8.5	6.5-8.5	600	250

ADWG 2011 Health 	0.003      0.003	0.01	0.01	0.002	0.002	2	2	0.01	0.01	0.02	0.02	500

WHO Guidelines for Drinking Water Quality (2011)	0.02	0.02	0.01	0.01	0.003	0.003	2	2	0.01	0.01	0.07	0.07	3	3

Field Observations

Property_ID	 Field_ID	 Sampled_Date_Time	 Sample_Type	 Appearance	 Odour 	SDG

1	1/5001_20140603	3/06/2014	tank tap	clear	none	EM1405428	0.01	0.008	<0.001	<0.001	0.0073	0.0042      0.006     0.004     <0.05    <0.05      0.003	0.002	0.001	0.001	4.71	3.54	-	6.96	30	<1

2	2/5001_20140604	4/06/2014	kitchen tap	clear	none	EM1405497	0.02	0.021	<0.001	<0.001	0.0005	0.0004      0.022     0.016     <0.05    <0.05    <0.001     <0.001      <0.001	0.002	2.31	1.94	7.37	7	28	1

2	2/5003_20140604	4/06/2014	outside tap	red brown particulates	none	EM1405497	0.019      0.022	<0.001	<0.001	0.0005	0.0004	0.21      0.052     <0.05    <0.05      0.016	0.001	0.001	<0.001	2.54	2.23	7.66	7.14	28	2

3	3/5001_20140603	3/06/2014	within tank	red brown particulates	none	EM1405428	0.007      0.004	<0.001	<0.001	0.0008	0.0006     <0.001   <0.001   <0.05    <0.05      0.004      <0.001      <0.001	<0.001	5.73	5.8	-	6.88	28	<1

4	4/5001_20140603	3/06/2014	tank tap	clear	none	EM1405428	0.023      0.021	<0.001	<0.001	0.0001      <0.0001     0.005     0.005     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	1.92	1.76	-	6.7	27	<1

5	5/5001_20140603	3/06/2014	within tank	clear	none	EM1405428	0.017      0.015	<0.001	<0.001      <0.0001     <0.0001    <0.001    0.002     <0.05     0.08      <0.001     <0.001      <0.001	<0.001	0.417      0.391	-	7.62	63	<1

5	5/5002_20140603	3/06/2014	kitchen tap	clear	none	EM1405428	0.017      0.016	<0.001	<0.001      <0.0001     <0.0001     0.007      0.01      <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	0.392      0.371	-	7.72	65	<1

6	6/5001_20140604	4/06/2014	within tank	clear	none	EM1405497	0.003      0.003	<0.001	<0.001      <0.0001     <0.0001     0.002     0.006     <0.05    <0.05      0.003	0.002	<0.001	<0.001	2.11	1.12	7.11	6.63	23	<1

6	6/5002_20140604	4/06/2014	kitchen tap	clear	none	EM1405497	0.002      0.001	<0.001	<0.001      <0.0001      0.0001      0.128     0.235      0.43	0.1	0.004	0.008	0.006	0.004	1.76	1.57	7.27	6.71	20	<1

7	7/5001_20140603	3/06/2014	kitchen tap	clear	none	EM1405428	0.005      0.003	<0.001	<0.001	0.0007      <0.0001     0.292     0.048      0.17     <0.05      0.004      <0.001      <0.001	<0.001	3.89	1.11	-	6.9	36	<1

7	7/5002_20140603	3/06/2014	outside tap	clear	none	EM1405428	0.011      0.011	<0.001	<0.001	0.0004	0.0002      0.071     0.034     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	2.36	1.88	-	7	33	<1

8	8/5001_20140603	3/06/2014	kitchen tap	clear	none	EM1405428	0.006      0.005	<0.001	<0.001      <0.0001     <0.0001     0.044     0.071     <0.05    <0.05      0.001      <0.001      <0.001	0.001	1.36	1.37	-	7.48	208	26

8	8/5002_20140603	3/06/2014	within tank	particulate matter in base of bailer	none	EM1405428	0.013      0.006	<0.001	<0.001      <0.0001     <0.0001     0.016     0.005      0.66     <0.05      0.017      <0.001      <0.001	<0.001	0.298      0.389	-	7.19	303	24

9	9/5001_20140602	2/06/2014	within tank	some black particulates	none	EM1405374	0.006      0.009	0.004	0.004	0.0002	0.0002      0.003     0.004     <0.05    <0.05      0.001      <0.001      <0.001	<0.001	0.797      0.615	-	6.87	12	<1

9	9/5002_20140602	2/06/2014	kitchen tap	clear	none	EM1405374	0.009      0.008	0.002	0.002	0.0001	0.0001      0.095     0.174     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	0.673      0.629	-	6.78	<10	<1

10	10/5002_20140604	4/06/2014	kitchen tank	clear	none	EM1405497	0.007      0.006	<0.001	<0.001	0.0002      <0.0001     0.684      0.14      <0.05    <0.05      0.001	0.002	<0.001	0.002	2.02	1.29	6.87	6.69	14	<1

10	10/5001_20140604	4/06/2014	within tank	clear	none	EM1405497	0.013      0.013	0.002	0.002	<0.0001     <0.0001     0.007     0.004     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	0.511      0.138	6.81	5.8	<10	<1

11	11/5001_20140605	5/06/2014	outside tap	clear	none	EM1405562	0.011      0.012	<0.001	<0.001	0.0002	0.0002      0.313      0.24      <0.05    <0.05      0.003	0.002	<0.001	<0.001	1.13	1.21	7.17	7.47	110	2

12	12/5001_20140604	4/06/2014	kitchen tap	clear	none	EM1405497	0.007      0.007	<0.001	<0.001      <0.0001     <0.0001     0.051     0.047     <0.05    <0.05      0.001	0.002	<0.001	<0.001	0.53	0.612	7.13	7.38	195	22

13	13/5001_20140603	3/06/2014	kitchen tap	clear	none	EM1405428	0.006      0.005	<0.001	<0.001	0.0004	0.0003      0.019     0.022     <0.05     0.08	0.001      <0.001      <0.001	<0.001	1.2	1.3	-	7.26	58	<1

13	13/5002_20140603	3/06/2014	within tank	clear	none	EM1405428	0.006      0.005	<0.001	<0.001	0.0001      <0.0001    <0.001   <0.001   <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	0.605      0.608	-	7.28	48	<1

14	14/5001_20140603	3/06/2014	kitchen tap	clear	none	EM1405428	0.014      0.014	<0.001	<0.001      <0.0001     <0.0001     0.052     0.026     <0.05    <0.05      0.001      <0.001	0.001	0.001	1.98	1.62	-	7.19	56	1

14	14/5002_20140603	3/06/2014	tank tap	black particulate matter observed	none	EM1405428	0.015      0.014	<0.001	<0.001	0.0002      <0.0001     0.122     0.004      0.13     <0.05	0.01	<0.001	0.001	0.001	2.28	1.74	-	7.17	55	<1

15	15/5003_20140604	4/06/2014	within tank	clear	none	EM1405497	0.004      0.004	<0.001	<0.001	0.0002	0.0001     <0.001    0.002     <0.05    <0.05      0.002	0.002	<0.001	0.001	5.68	4.44	7.07	6.86	26	1

15	15/5001_20140604	4/06/2014	kitchen tap	clear	none	EM1405497	0.002      0.002	<0.001	<0.001      <0.0001     <0.0001     0.004     0.008     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	0.414      0.337	7.3	7.08	21	2

16	16/5001_20140602	2/06/2014	kitchen tap	clear	none	EM1405374	0.004      0.006	<0.001	<0.001	0.0008	0.0004      0.084     0.045     <0.05    <0.05      0.001      <0.001	0.002	0.001	0.811      0.805	-	6.94	12	<1

16	16/5002_20140602	2/06/2014	tank tap	clear	none	EM1405374	0.014      0.013	<0.001	<0.001	0.0003	0.0002      0.063     0.017     <0.05    <0.05      0.003	0.001	<0.001	0.001	0.336	0.31	-	3.79	20	<1

18	18/5001_20140603	3/06/2014	within tank	clear, trace black particulate matter	none	EM1405428	0.065      0.046	<0.001	<0.001      <0.0001     <0.0001     0.018      0.01      <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	1.78	1.3	-	7.31	71	<1

18	18/5002_20140603	3/06/2014	kitchen tap	clear	none	EM1405428	0.059      0.053	<0.001	<0.001      <0.0001     <0.0001      0.34      0.216     <0.05    <0.05      0.004	0.004	<0.001	<0.001	1.86	1.61	-	7.28	55	<1

20	20/5001_20140604	4/06/2014	within tank	clear	none	EM1405497	0.021      0.024	<0.001	<0.001      <0.0001     <0.0001    <0.001    0.004     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	0.143      0.178	6.94	7.77	34	1

20	20/5002_20140604	4/06/2014	kitchen tap	clear	none	EM1405497	0.024      0.027	<0.001	<0.001      <0.0001      0.0001      0.019     0.027     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	0.352      0.441	7.01	7.08	21	1

21	21/5001_20140603	3/06/2014	tank tap	clear	none	EM1405428	0.015      0.011	<0.001	<0.001      <0.0001     <0.0001      0.24      0.325     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	2.81	4.85	-	6.91	40	<1

21	21/5002_20140603	3/06/2014	kitchen tap	clear	none	EM1405428	0.018      0.014	<0.001	<0.001	0.0001      <0.0001      2.17	1.02      <0.05    <0.05      0.005	0.002	<0.001	<0.001	0.413	0.22	-	6.71	29	<1

22	22/5004_20140605	5/06/2014	within tank	clear	none	EM1405562	0.086      0.087	<0.001	<0.001      <0.0001     <0.0001     0.001     0.002     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	1.23	1.44	6.05	7.38	90	1

22	22/5001_20140603	3/06/2014	tank tap	clear	none	EM1405428	0.047      0.043	<0.001	<0.001	0.0002      <0.0001     0.008     0.006     <0.05    <0.05      0.006	0.004	<0.001	<0.001	0.385	0.32	-	7.57	69	<1

22	22/5002_20140603	3/06/2014	within tank	clear	none	EM1405428	0.045	0.02	<0.001	<0.001	0.0001	0.0002      0.002     0.034     <0.05    <0.05      0.005	0.002	<0.001	<0.001	0.269      0.862	-	7.63	76	<1

22	22/5003_20140605	5/06/2014	within tank	pale yellow	none	EM1405562	0.061      0.065	<0.001	<0.001      <0.0001     <0.0001     0.055     0.028     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	0.342      0.253	NA 	4.62	26	1

23	23/5001_20140605	5/06/2014	within tank	clear	none	EM1405562	0.022      0.022	<0.001	<0.001      <0.0001     <0.0001     0.011     0.008     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	0.284	0.27	6.55	6.92	67	4

23	23/5002_20140605	5/06/2014	outside tap	pale yellow	none	EM1405562	0.028      0.012	<0.001	<0.001      <0.0001     <0.0001     0.086     0.078      0.35	0.22	0.003	0.001	0.001	0.003	0.088      0.257	6.55	6.86	201	6

24	24/5001_20140605	5/06/2014	tank tap	clear	none	EM1405562	0.005      0.005	<0.001	<0.001	0.0095	0.0068      0.008     0.007     <0.05    <0.05      0.002	0.001	<0.001	0.001	3.29	2.85	6.93	6.8	59	2

26	26/5001_20140603	3/06/2014	outside tap	clear	none	EM1405428	0.019      0.022	<0.001	<0.001      <0.0001     <0.0001      0.03      0.114     <0.05    <0.05      0.006	0.009	<0.001	0.002	0.865      0.983	-	6.54	29	<1

27	27/5001_20140604	4/06/2014	within tank	clear	none	EM1405497	0.009      0.009	<0.001	<0.001	0.0008	0.0005      0.004     0.005     <0.05    <0.05    <0.001     <0.001      <0.001	0.001	0.635      0.463	7.13	6.83	18	<1

27	27/5002_20140604	4/06/2014	kitchen tap	clear	none	EM1405497	0.008      0.009	<0.001	0.001	0.0003      <0.0001     0.056     0.017     <0.05    <0.05      0.001      <0.001	0.001	0.001	0.287      0.084	7.24	5.71	<10	<1

28	28/5001_20140604	4/06/2014	within tank	clear	none	EM1405497	0.004      0.005	<0.001	<0.001	0.0001	0.0001     <0.001    0.004     <0.05    <0.05      0.002	0.001	<0.001	<0.001	2.6	2.88	7.04	7.14	56	<1

30	30/5001_20140605	5/06/2014	within tank	clear	none	EM1405562	0.006      0.004	<0.001	0.001	<0.0001     <0.0001     0.007      0.01	0.14	0.08	0.006	0.005	0.002	0.002	1.98	2.12	6.11	6.38	96	<1

32	32/5001_20140605	5/06/2014	outside tap	clear	none	EM1405562	0.02	0.021	<0.001	<0.001      <0.0001     <0.0001     0.021     0.011     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	0.058      0.109	7.24	7.53	204	<1

34	34/5002_20140605	5/06/2014	outside tap	clear	none	EM1405562	0.099      0.107	<0.001	<0.001      <0.0001     <0.0001      0.64      0.092     <0.05    <0.05      0.002      <0.001      <0.001	<0.001	0.966      0.941	5.83	6.95	70	5

34	34/5001_20140605	5/06/2014	within tank	clear	none	EM1405562	0.106	0.11	<0.001	<0.001	0.0001      <0.0001    <0.001    0.002     <0.05    <0.05      0.001      <0.001      <0.001	<0.001	0.926      0.654	6.08	4.52	72	2

36	36/5001_20140602	2/06/2014	kitchen tap	clear	none	EM1405374	0.008      0.004	<0.001	<0.001	0.0001      <0.0001     0.074     0.071     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	6.68	6.37	-	6.94	18	<1

37	37/5001_20140605	5/06/2014	kitchen tap	clear	none	EM1405562	0.036      0.038	<0.001	<0.001      <0.0001      0.0001	1.42      0.647      0.09     <0.05      0.003	0.006	0.001	0.003	5.77	4.21	7	6.94	58	<1

37	37/5003_20140605	5/06/2014	within tank	clear	none	EM1405562	0.038      0.039	<0.001	<0.001      <0.0001     <0.0001     0.001     0.006	0.1	0.06      <0.001     <0.001      <0.001	<0.001	3.57	2.79	6.91	6.84	48	<1

40	40/5002_20140602	2/06/2014	within tank	slight yellow containing fibrous material	none	EM1405374	0.007      0.007	<0.001	<0.001      <0.0001     <0.0001     0.518     0.203     <0.05    <0.05      0.004	0.004	0.001	0.001	0.135      0.082	7.37	6.64	15	<1

40	40/5001_20140602	2/06/2014	kitchen tap	clear	none	EM1405374	0.008      0.008	<0.001	<0.001      <0.0001     <0.0001     0.006     0.008     <0.05    <0.05    <0.001     <0.001      <0.001	0.001	0.069      0.046	-	6.08	<10	<1

41	41/5001_20140604	4/06/2014	tank tap	clear	none	EM1405497	0.015      0.015	<0.001	<0.001	0.0004	0.0004      0.008     0.014     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	0.42	0.529	7.35	7.25	70	2

42	42/5001_20140605	5/06/2014	within tank	clear	none	EM1405562	0.025      0.026	<0.001	<0.001      <0.0001     <0.0001     0.002     0.003     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001     <0.005     0.006	7.18	7.2	51	<1

42	42/5002_20140605	5/06/2014	kitchen tap	clear	none	EM1405562	0.025      0.027	<0.001	<0.001      <0.0001     <0.0001     0.022     0.021     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001     <0.005   <0.005	7.21	7.18	50	1

43	43/5002_20140605	5/06/2014	kitchen tap	clear	none	EM1405562	<0.001    <0.001     <0.001	<0.001      <0.0001     <0.0001      1.27      0.056     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001	0.035     <0.005	5.7	6.43	10	<1

43	43/5001_20140605	5/06/2014	within tank	clear	none	EM1405562	<0.001    <0.001     <0.001	<0.001      <0.0001     <0.0001     0.007     0.004     <0.05    <0.05    <0.001     <0.001      <0.001	<0.001     <0.005   <0.005	5.85	5.31	<10	<1

Statistical Summary

Number of Results	69	69	69	69	69	69	69	69	69	69	69	69	69	69	69	69	41	69	69	69

Number of Detects	67	67	3	5	35	28	62	67	10	7	36	27	12	22	66	66	41	69	63	26

Minimum Concentration	<0.001    <0.001     <0.001	<0.001      <0.0001     <0.0001    <0.001   <0.001   <0.05    <0.05    <0.001     <0.001      <0.001	<0.001     <0.005   <0.005	5.7	3.79	<10	<1

Minimum Detect	0.002      0.001	0.002	0.001	0.0001	0.0001      0.001     0.002      0.09	0.06	0.001	0.001	0.001	0.001	0.035      0.006	5.7	3.79	10	1

Maximum Concentration	0.106	0.11	0.004	0.004	0.0098	0.0097	2.17	1.02	0.66	0.22	0.017	0.009	0.006	0.005	6.68	6.37	7.66	7.77	303	26

Maximum Detect	0.106	0.11	0.004	0.004	0.0098	0.0097	2.17	1.02	0.66	0.22	0.017	0.009	0.006	0.005	6.68	6.37	7.66	7.77	303	26

Average Concentration	0.019      0.019     0.00059     0.00061     0.00055     0.00043      0.15      0.077     0.061    0.033     0.0022     0.0014     0.00069     0.00088	1.6	1.5	6.9	6.8	53	2

Median Concentration	0.013      0.011	0.0005	0.0005	0.0001	0.00005     0.019     0.017     0.025    0.025      0.001      0.0005      0.0005	0.0005	0.926      0.941	7.02	6.94	36	0.5

Standard Deviation	0.022      0.022     0.00049     0.00049	0.0018	0.0015	0.36	0.16	0.12     0.028     0.0031     0.0018     0.00071     0.00084	1.6	1.6	0.47	0.72	55	4.8

Number of Guideline Exceedances	63	61	0	0	3	3	3	1	4	0	2	0	0	0	12	10	6	10	0	0

Number of Guideline Exceedances(Detects Only)	63	61	0	0	3	3	3	1	4	0	2	0	0	0	12	10	6	10	0	0

16/06/2014	Page 1 of 1

ATTACHMENT A

Sampling Methodology

| Item | Description |
| --- | --- |
| Sample Date | 2, 3, 4 and 5 June 2014. The following weather observations were made during the sampling event:  2 June 2014 – overcast  3 June 2014 – overcast, light showers in the morning  4 June 2014 – foggy in the morning, sunny afternoon  5 June 2014 – overcast (ground conditions very wet from overnight rain) |
| Adopted Sampling Guidelines | Australian/New Zealand Standard 5667.1 (1998) Water Quality – Sampling Part 1: Guidance on the design of sampling programs, sampling techniques and the preservation and handling of samples. This Standard provides general principles to be applied in sampling for the physical, chemical, microbiological or radiological analysis of waters and waste waters, including bottom sediment and sludges, for the purposes of process control, quality characterization, identification of sources of pollution and the monitoring of background levels. The guidance on sampling procedures provided in this Standard is generally applicable. Where alternative procedures are used they are to be demonstrated to be at least as reliable as those provided in this Standard or that they will achieve the objectives of the sampling and analysis program. Australian/New Zealand Standard 5667.5 (1998) Water Quality – Sampling Part 5: Guidance on sampling of drinking water and water used for food and beverage processing. This is Part 5 in a series of Standards on the sampling of waters, waste waters, sediments and sludges. The objective this series of standards is to provide parties interested in monitoring and techniques, preservation, handling and transport of samples for the purposes of process control, quality characterisation, identification of sources of pollution, compliance with water quality guidelines or standards, and other activities. This part of the series provides detailed principles to be applied to the sampling of drinking water and water used for food and beverage processing. |
| Sample Points |  Rainwater tank (sample collected within the tank).  Kitchen tap (sample collected when a resident was present to provide access).  Rainwater tank tap (collected when a tap was present and a sample could not be collected from within the tank due to logistical constraints).  Outdoor tap (collected when a garden tap was present and a resident was not present to provide access to the kitchen tap). |
| Number of Primary Samples Collected |  Rainwater tank – 22 samples  Kitchen tap – 21 samples  Rainwater tank tap - 8 samples |

| Item | Description |
| --- | --- |
|  |  Outdoor tap – 7 samples |
| Rainwater tank sample collection methodology | Tank water samples were collected within the tank at approximately 30 cm to 50 cm below the water surface using a high density polyethylene foot valve and tubing. Water was transferred directly into sample bottles from the tubing with no contact between tubing and bottles. All hosing and foot valves were stored in clean packaging prior to use from the supplier and the sampling equipment was replaced between rainwater tanks. |
| Tap sample collection methodology |  Initial draw off (all tap sample points) – water was collected from the initial draw off water as this was considered to represent the sample with the highest potential sediment load.  Post flush (10 tap sample points) – samples were collected after 2 to 3 minutes of water flow as per Australian/New Zealand Standard 5667.5 to assess the effect of flush out of stale water. The comparison of results from each sample collection methodology is discussed further in item ‘comparison of pre and post flush tap samples’ in Attachment B. |
| Field Data | At 20 sample points, the pH and conductivity was measured in a bucket using a water quality meter. |
| Record of Sample Location | Sampling locations were recorded with hand-held GPS with +/- 10 m accuracy. |
| Sample Storage | Samples were transferred into appropriately preserved bottles supplied by the NATA accredited laboratory. |
| Sample Delivery | The samples were transferred into chilled, insulated containers and delivered to the laboratory under Chain of Custody (CoC) procedures. |
| Laboratory for Water Analysis | The laboratory engaged as the primary laboratory for the analysis was ALS Environmental Pty Ltd which is registered by the National Association of Testing Authority (NATA) for the analyses performed. The secondary laboratory selected for quality assurance testing was MGT Eurofins. |
| Laboratory Analytical Schedule | Selected samples were designated for analysis of total dissolved solids, pH, sulphate, total and dissolved metals (including antimony, arsenic, cadmium, copper, iron, lead, nickel and zinc). |
| Adopted Assessment Criteria |  World Health Organisation Guidelines for Drinking Water Quality, 2011 (WHO Guidelines). The Guidelines provide the recommendations of the World Health Organisation for managing the risk from hazards that may compromise the safety of drinking-water. The Guidelines describe reasonable minimum requirements of safe practice to protect the health of consumers and derive numerical “guideline values” for constituents of water of indicators of water quality. The Guidelines state that when defining mandatory limits, it is preferable to consider the Guidelines in the context of location or national environmental, social, economic and cultural conditions.  National Water Quality Management Strategy Australian Drinking Water Guidelines 6 Version 2.0, 2011 (ADWG). The ADWG are derived so as to take account of the needs of an individual through a normal lifetime, including changes in sensitivity that may occur between life stages. The ADWG includes both health related guideline values and aesthetic guideline values. |
|  | Health related guideline values: concentration or measure of a water quality characteristic that, based on present knowledge, does not result in any significant risk to the health of the consumer over a lifetime of consumption. The adopted antimony value is a health related guideline value. Aesthetic related guideline values: concentration or measure of a water quality characteristic that is associated with acceptability of water to the consumer; for example, appearance, taste, odour. |

ATTACHMENT B

Data Quality Assurance and Quality Control

| Item | Description |
| --- | --- |
| QA/QC Objectives |
| Data Quality Measures and Objectives | The data quality measures for the assessment are as follows: Accuracy: A measure of the closeness of the results to the actual results. Accuracy is assessed through the comparison of results produced by the primary and secondary laboratories for the same sample and by the measuring of the extent to which an analytical result reflects the known concentration as measured by the recovery obtained from internal laboratory spikes. Precision: A measure of the repeatability of results by the laboratory. This is assessed through the analysis of duplicates both internally and externally. Completeness: The percentage of acceptable data obtained compared to the amount of data needed to achieve a particular level of confidence in the results. The following data quality objectives (DQOs) have been set for this project: primary samples and field duplicates recording Relative Percentage Differences (RPDs) less than 30% for inorganics and less than 50% for organics; primary samples and primary laboratory internal duplicates recording RPDs less than 30% for inorganics and less than 50% for organics; accuracy in spike samples to range between 70% and 130% (for organics and other inorganics); rinsate blanks and primary laboratory method blanks below practical quantitation limits (PQLs), or equal or less than background levels, wherever justified; overall data quality completeness of 95% or greater. The primary and secondary duplicate results for chemical data were compared with primary sample results using RPDs. RPDs were calculated according to the following formula: Where: ABS – absolute number A – concentration of the primary laboratory result per analyte B – concentration of corresponding duplicate result. RPD values can range from 0% (indicating perfect correlation between results) to 200% (indicating complete divergence in results). |

| Item | Description |
| --- | --- |
| QA/QC Methodology |
| QA/QC Sample Collection | The following QA/QC samples were collected: Primary duplicate samples at a frequency of 10.3% against primary samples. Secondary duplicate samples at a frequency of 6.9% against secondary samples. A total of 11 rinsate samples from clean plastic equipment used in the sampling process including tubing, foot valves, filters and syringers. The purpose of the rinsates was to assess the potential for antimony, if a component of the sample material, to leach into the sample. One container blank using a preserved sample bottle provided by ALS Environmental for total and dissolved metals analysis. This blank was undertaken to assess the potential for antimony, if present in the bottle composition, to leach from the sample bottle into the sample. Ten water samples from taps following after 2 to 3 minutes of water flow as per Australian/New Zealand Standard 5667.5 to assess the effect of flush out of stale water. It is noted that AS/NZS 5667.1 recommends taking a transport blank (also known as trip blank) to estimate the amount of contamination introduced during the transport and storage of samples from the time of sampling until the time of analysis. Given that the chemicals of interest are not volatile and samples were stored in sealed containers, this contamination pathway did not warrant investigation. |
| Minimisation of cross-contamination | Golder staff used new nitrile gloves for collection of each water sample and decontaminated reusable equipment between each sampling point. |
| Sample Handling and Preservation | Water samples were collected into laboratory supplied vessels containing appropriate preservatives for the selected analysis. The collected samples were immediately placed in a chilled and insulated container with ice and stored in this manner prior to and during transit to the laboratory. |
| Equipment Calibration | The water quality meter was calibrated prior to use for each day of sampling. A copy of the calibration certificates is provided at the back of this attachment. |
| Laboratory internal QC | The quality of the laboratory data generated was supported with appropriate laboratory Quality Control (QC) samples and assessed using standard methods. Internal laboratory QC samples including method blanks, laboratory duplicates, matrix spikes, laboratory control sample spikes and surrogate spikes were analysed as part of the quality assurance program. |

| Item | Description |
| --- | --- |
| QA/QC Results |
| Summary of Groundwater QA/QC Results | QC Sample Type Number of Results NOT Meeting Data Quality Objectives Total Number of Results (Individual Analytes) Percentage Meeting Data Quality Objectives Primary Duplicates 4 114 96.5% Secondary Duplicates 8 76 89.5% Rinsates 0 176 100% Internal Duplicates 8 271 97.0% Matrix Spikes 0 100 100% Method Blanks 0 163 100% Overall Completeness 20 900 97.8% |
| Discussion of results | Six primary duplicate and four secondary duplicate samples were analysed during the assessment and a total 58 primary water samples analysed. This equates to an analysis frequency of 10.3% and 6.9% for collection of primary and secondary duplicates respectively. This complies with the specified collection rate of 5%. Primary and secondary analytical results are presented in Table B-1 at the back of this attachment. Of the 114 primary duplicate analytes, four returned RPDs above 50%, representing a conformance level of 97.8%. Of the 104 secondary duplicate analytes, 8 returned RPDs above 50%, representing a conformance level of 89.5%. Non-conformances, with RPDs ranging between 51% and 152%, were observed for metals including total cadmium, total iron, total lead, total zinc and filtered copper. Five of the 8 RPD non-conformances were between 51% and 67%. It is considered unlikely that the non-conformance will affect the overall quality or outcome of the assessment and is not related to reporting of antimony. None of the 176 rinsate analysis results reported levels above the laboratory limit of reporting. This represents compliance of 100.0% indicating that the plastics used during water sampling were an unlikely source of antimony detected in the water samples. A review of the RPDs for the Internal Duplicate tests indicates that 8 of the 271 tests conducted did not produce results within the desired 30% RPD conformance limit. This result represents a compliance of 97.0%. Non-conformances were observed for Antimony, Copper, Lead and Zinc. Three non-conformances were observed for the chemical of interest, Antimony, each with an RPD of 66%. This RPD is attributed to the low levels of detection in the samples. The exceedance is not considered to impact on the overall quality or outcome of the assessment. A review of the 100 Matrix Spike results indicates that all analyses provided a recovery beyond 70-130%, representing a conformance level of 100%. A review of the Method Blank tests indicates that all of the 163 laboratory internal blanks analytes were below laboratory reporting limit, representing compliance of 100%. The achieved QA/QC completeness of 97.8% is above the overall completeness objective of 95%. Based on this, it is considered that the overall data quality generated during the assessment of water by Golder Associates is of sufficient quality upon which to base decisions for this assessment. |
| Additional Quality Assurance Checks |
| Comparison of pre and post flush tap samples | Total antimony concentrations: three post flush samples reported higher concentrations than pre flush samples by between 0.001 and 0.002 mg/L; three post flush samples reported lower concentrations than the pre flush samples; and four samples reported the same concentration. Dissolved antimony concentrations: three post flush samples reported higher concentrations than pre flush samples by 0.001 mg/L; seven samples reported the same concentration. Based on the above summary, Golder Associates considers that the time at which a sample is collected from the tap does not impact upon the quality of the data collected. The pre flush samples are therefore considered appropriate for the objectives of the sampling and analysis program. |
| Comparison of field and laboratory reported pH | pH was measured in the field and laboratory for 41 samples. The results are presented in Table A and are summarised below. 26 laboratory reported pH was less than the field reported pH. The difference in pH ranged between 0.03 units and 1.56 units. 15 laboratory reported pH was greater than the field reported pH. The difference in pH ranged between 0.02 units and 1.33 units. |
| Comparison of dissolved antimony concentrations to total dissolved antimony concentrations | 20 of the dissolved concentrations were greater than the total dissolved concentrations, in 20 of the 58 samples analysed. The difference between the total and dissolved antimony concentrations ranged between 0.001 mg/L and 0.008 mg/L and is attributable to the following factors: Laboratory reported measurement of uncertainty of approximately +/-13% for dissolved and total antimony concentrations in water. The reported measurement of uncertainty is a factor in all laboratory analysis undertaken and the reported uncertainty in this case is acceptable for the objectives of the assessment. Separate sample bottles are filled for the analysis of total and dissolved antimony. There will be slight variations in water composition between each sample bottle. |

Primary Duplicates

Table B-1: Primary and Secondary Duplicate  Analytical Results	Rainwater Tank Monitoring

Costerfield

147613051

| Chem_Group | ChemName | Units | EQL |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Heavy Metals | Antimony | mg/l | 0.001 : 0.005 (Interlab) | 0.014 | 0.014 | 0 | 0.015 | 0.015 | 0 | 0.007 | 0.005 | 33 | 0.006 | 0.006 | 0 |
|  | Antimony (Filtered) | mg/l | 0.001 : 0.005 (Interlab) | 0.014 | 0.014 | 0 | 0.014 | 0.014 | 0 | 0.004 | 0.004 | 0 | 0.005 | 0.005 | 0 |
|  | Arsenic | mg/l | 0.001 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Arsenic (Filtered) | mg/l | 0.001 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Cadmium | mg/l | 0.0001 : 0.0002 (Interlab) | <0.0001 | 0.0001 | 0 | 0.0002 | <0.0001 | 67 | 0.0008 | 0.0009 | 12 | 0.0004 | 0.0004 | 0 |
|  | Cadmium (Filtered) | mg/l | 0.0001 : 0.0002 (Interlab) | <0.0001 | <0.0001 | 0 | <0.0001 | <0.0001 | 0 | 0.0006 | 0.0006 | 0 | 0.0003 | 0.0003 | 0 |
|  | Copper | mg/l | 0.001 | 0.052 | 0.063 | 19 | 0.122 | 0.024 | 134 | <0.001 | <0.001 | 0 | 0.019 | 0.012 | 45 |
|  | Copper (Filtered) | mg/l | 0.001 | 0.026 | 0.03 | 14 | 0.004 | 0.002 | 67 | <0.001 | <0.001 | 0 | 0.022 | 0.019 | 15 |
|  | Iron | mg/l | 0.05 | <0.05 | <0.05 | 0 | 0.13 | 0.08 | 48 | <0.05 | <0.05 | 0 | <0.05 | <0.05 | 0 |
|  | Iron (Filtered) | mg/l | 0.05 | <0.05 | <0.05 | 0 | <0.05 | <0.05 | 0 | <0.05 | <0.05 | 0 | 0.08 | 0.09 | 12 |
|  | Lead | mg/l | 0.001 | 0.001 | 0.001 | 0 | 0.01 | 0.003 | 108 | 0.004 | 0.004 | 0 | 0.001 | 0.001 | 0 |
|  | Lead (Filtered) | mg/l | 0.001 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 | <0.001 | 0.001 | 0 |
|  | Nickel | mg/l | 0.001 | 0.001 | 0.001 | 0 | 0.001 | 0.001 | 0 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Nickel (Filtered) | mg/l | 0.001 | 0.001 | <0.001 | 0 | 0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Zinc | mg/l | 0.005 : 0.001 (Interlab) | 1.98 | 1.96 | 1 | 2.28 | 2.08 | 9 | 5.73 | 5.77 | 1 | 1.2 | 1.16 | 3 |
|  | Zinc (Filtered) | mg/l | 0.005 : 0.001 (Interlab) | 1.62 | 1.87 | 14 | 1.74 | 1.93 | 10 | 5.8 | 5.76 | 1 | 1.3 | 1.39 | 7 |
| Sample Quality Parameters | pH (Lab) | pH_Units | 0.01 : 0.1 (Interlab) | 7.19 | 7.18 | 0 | 7.17 | 7.19 | 0 | 6.88 | 6.92 | 1 | 7.26 | 7.25 | 0 |
|  | Total Dissolved Solids @180°C | mg/l | 10 | 56 | 61 | 9 | 55 | 62 | 12 | 28 | 38 | 30 | 58 | 65 | 11 |
|  | Sulphate (as SO4) (Filtered) | mg/l | 1 | 1 | <1 | 0 | <1 | <1 | 0 | <1 | <1 | 0 | <1 | <1 | 0 |

*RPDs have only been considered where a concentration is greater than 0 times the EQL

**High RPDs are in bold (Acceptable RPDs for each EQL multiplier range are: 50 (0-10 x EQL); 50 (10-30 x EQL); 50 ( > 30 x EQL)

***Interlab Duplicates are matched on a per compound  basis as methods vary between  laboratories.   Any methods in the row header relate to those used in the primary laborator

Primary Duplicates

| Chem_Group | ChemName | Units | EQL |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Heavy Metals | Antimony | mg/l | 0.001 : 0.005 (Interlab) | 0.023 | 0.023 | 0 | 0.006 | 0.006 | 0 |
|  | Antimony (Filtered) | mg/l | 0.001 : 0.005 (Interlab) | 0.021 | 0.021 | 0 | 0.005 | 0.005 | 0 |
|  | Arsenic | mg/l | 0.001 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Arsenic (Filtered) | mg/l | 0.001 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Cadmium | mg/l | 0.0001 : 0.0002 (Interlab) | 0.0001 | <0.0001 | 0 | 0.0001 | <0.0001 | 0 |
|  | Cadmium (Filtered) | mg/l | 0.0001 : 0.0002 (Interlab) | <0.0001 | <0.0001 | 0 | <0.0001 | <0.0001 | 0 |
|  | Copper | mg/l | 0.001 | 0.005 | 0.005 | 0 | <0.001 | <0.001 | 0 |
|  | Copper (Filtered) | mg/l | 0.001 | 0.005 | 0.005 | 0 | <0.001 | <0.001 | 0 |
|  | Iron | mg/l | 0.05 | <0.05 | <0.05 | 0 | <0.05 | <0.05 | 0 |
|  | Iron (Filtered) | mg/l | 0.05 | <0.05 | <0.05 | 0 | <0.05 | <0.05 | 0 |
|  | Lead | mg/l | 0.001 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Lead (Filtered) | mg/l | 0.001 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Nickel | mg/l | 0.001 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Nickel (Filtered) | mg/l | 0.001 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Zinc | mg/l | 0.005 : 0.001 (Interlab) | 1.92 | 1.92 | 0 | 0.605 | 0.593 | 2 |
|  | Zinc (Filtered) | mg/l | 0.005 : 0.001 (Interlab) | 1.76 | 1.06 | 50 | 0.608 | 0.626 | 3 |
| Sample Quality Parameters | pH (Lab) | pH_Units | 0.01 : 0.1 (Interlab) | 6.7 | 7.32 | 9 | 7.28 | 7.26 | 0 |
|  | Total Dissolved Solids @180°C | mg/l | 10 | 27 | 30 | 11 | 48 | 56 | 15 |
|  | Sulphate (as SO4) (Filtered) | mg/l | 1 | <1 | <1 | 0 | <1 | <1 | 0 |

*RPDs have only been considered where a concentration is greater than 0 times the EQL

**High RPDs are in bold (Acceptable RPDs for each EQL multiplier range are: 50 (0-10 x EQL); 50 (10-30 x EQL); 50 ( > 30 x EQL)

***Interlab Duplicates are matched on a per compound  basis as methods vary between  laboratories.   Any methods in the row header relate to those used in the primary laborator

Secondary Dulplicates

| Chem_Group | ChemName | Units | EQL |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Heavy Metals | Antimony | mg/l | 0.001 : 0.005 (Interlab) | 0.007 | <0.005 | 33 | 0.006 | <0.005 | 18 | 0.014 | 0.01 | 33 | 0.023 | 0.015 | 42 |
|  | Antimony (Filtered) | mg/l | 0.001 : 0.005 (Interlab) | 0.004 | <0.005 | 22 | 0.005 | <0.005 | 0 | 0.014 | 0.01 | 33 | 0.021 | 0.015 | 33 |
|  | Arsenic | mg/l | 0.001 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Arsenic (Filtered) | mg/l | 0.001 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Cadmium | mg/l | 0.0001 : 0.0002 (Interlab) | 0.0008 | 0.0006 | 29 | 0.0004 | 0.0002 | 67 | <0.0001 | <0.0002 | 0 | 0.0001 | <0.0002 | 67 |
|  | Cadmium (Filtered) | mg/l | 0.0001 : 0.0002 (Interlab) | 0.0006 | 0.0006 | 0 | 0.0003 | 0.0003 | 0 | <0.0001 | <0.0002 | 0 | <0.0001 | <0.0002 | 0 |
|  | Copper | mg/l | 0.001 | <0.001 | 0.001 | 0 | 0.019 | 0.017 | 11 | 0.052 | 0.063 | 19 | 0.005 | 0.007 | 33 |
|  | Copper (Filtered) | mg/l | 0.001 | <0.001 | 0.001 | 0 | 0.022 | 0.016 | 32 | 0.026 | 0.048 | 59 | 0.005 | 0.007 | 33 |
|  | Iron | mg/l | 0.05 | <0.05 | 0.32 | 146 | <0.05 | 0.12 | 82 | <0.05 | 0.37 | 152 | <0.05 | <0.05 | 0 |
|  | Iron (Filtered) | mg/l | 0.05 | <0.05 | <0.05 | 0 | 0.08 | <0.05 | 46 | <0.05 | <0.05 | 0 | <0.05 | <0.05 | 0 |
|  | Lead | mg/l | 0.001 | 0.004 | 0.008 | 67 | 0.001 | 0.001 | 0 | 0.001 | 0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Lead (Filtered) | mg/l | 0.001 | <0.001 | <0.001 | 0 | <0.001 | 0.001 | 0 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Nickel | mg/l | 0.001 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 | 0.001 | 0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Nickel (Filtered) | mg/l | 0.001 | <0.001 | <0.001 | 0 | <0.001 | <0.001 | 0 | 0.001 | 0.001 | 0 | <0.001 | <0.001 | 0 |
|  | Zinc | mg/l | 0.005 : 0.001 (Interlab) | 5.73 | 9.7 | 51 | 1.2 | 1.3 | 8 | 1.98 | 2 | 1 | 1.92 | 2 | 4 |
|  | Zinc (Filtered) | mg/l | 0.005 : 0.001 (Interlab) | 5.8 | 7.4 | 24 | 1.3 | 1.3 | 0 | 1.62 | 2 | 21 | 1.76 | 2 | 13 |
| Sample Quality Parameters | pH (Lab) | pH_Units | 0.01 : 0.1 (Interlab) | 6.88 | 6 | 14 | 7.26 | 6.5 | 11 | 7.19 | 6.6 | 9 | 6.7 | 6.4 | 5 |
|  | Total Dissolved Solids @180°C | mg/l | 10 | 28 | 31 | 10 | 58 | 59 | 2 | 56 | 76 | 30 | 27 | 36 | 29 |
|  | Sulphate (as SO4) (Filtered) | mg/l | 1 | <1 |  |  | <1 |  |  | 1 |  |  | <1 |  |  |

*RPDs have only been considered where a concentration is greater than 0 times the EQL

**High RPDs are in bold (Acceptable RPDs for each EQL multiplier range are: 50 (0-10 x EQL); 50 (10-30 x EQL); 50 ( > 30 x EQL)

***Interlab Duplicates are matched on a per compound  basis as methods vary between  laboratories.   Any methods in the row header relate to those used in the primary laborator

13/06/2014	Page 1 of 1

ATTACHMENT C

Limitations

16 June 2014

Report No. 147613051-004-L-Rev0

# LIMITATIONS

This Document has been provided by Golder Associates Pty Ltd (“Golder”)

subject to the following limitations:

This  Document  has  been  prepared  for  the  particular  purpose  outlined  in Golder’s  proposal  and  no  responsibility  is  accepted  for  the  use  of  this Document, in whole or in part, in other contexts or for any other purpose.

The scope and the period of Golder’s Services are as described in Golder’s proposal, and are subject to restrictions and limitations.  Golder did not perform a complete assessment of all possible conditions or circumstances that may exist at the site referenced in the Document.  If a service is not expressly indicated, do not assume it has been provided.  If a matter is not addressed, do not assume that any determination has been made by Golder in regards to it.

Conditions may exist which were undetectable given the limited nature of the enquiry Golder was retained to undertake with respect to the site.  Variations in conditions may occur between investigatory locations, and there may be special conditions pertaining to the site which have not been revealed by the investigation and which have not therefore been taken into account in the Document. Accordingly, additional studies and actions may be required.

In addition, it is recognised that the passage of time affects the information and assessment provided in this Document.  Golder’s opinions are based upon information that existed at the time of the production of the Document.   It is understood that the Services provided allowed Golder to form no more than an opinion of the actual conditions of the site at the time the site was visited and cannot be used to assess the effect of any subsequent changes in the quality of the site, or its surroundings, or any laws or regulations.

Any assessments made in this Document are based on the conditions indicated from  published  sources  and  the  investigation  described.  No  warranty  is included, either express or  implied, that  the actual conditions will conform exactly to the assessments contained in this Document.

Where data supplied by the client or other external sources, including previous site  investigation  data,  have  been  used,  it  has  been  assumed  that  the information is correct unless otherwise stated. No responsibility is accepted by Golder for incomplete or inaccurate data supplied by others.

Golder may have retained subconsultants affiliated with Golder to provide Services for the benefit of Golder.  To the maximum extent allowed by law, the Client acknowledges and agrees it will not have any direct legal recourse to, and waives any claim, demand, or cause of action against, Golder’s affiliated companies, and their employees, officers and directors.

This Document is provided for sole use by the Client and is confidential to it and its professional advisers. No responsibility whatsoever for the contents of this Document will be accepted to any person other than the Client.  Any use which a third party makes of this Document, or any reliance on or decisions to be made based on it, is the responsibility of such third parties.  Golder accepts no responsibility for damages, if any, suffered by any third party as a result of decisions made or actions based on this Document.

GOLDER ASSOCIATES  PTY LTD	GAP Form No.  LEG 04  RL 1

APPENDIX B

Soil Monitoring – Factual Report

17 June 2014

Report No. 147613051-001-R-Rev1

16 June 2014	Reference No. 147613051-004-L-Rev0

Mr John Mitas

Chair of Government Reference Group

Operations General Manager

Department of State Development, Business and Innovation

Level 9, 121 Exhibition Street

Melbourne, 3000

Victoria

SOIL MONITORING FACTUAL REPORT, COSTERFIELD

Dear John

# 1.0	INTRODUCTION

Golder Associates Pty Ltd (Golder) was commissioned by the Department of State Development, Business and Innovation (DSDBI) to undertake a preliminary assessment of shallow surface soils in Costerfield, Victoria (the assessment area).

# 2.0	OBJECTIVE AND SCOPE OF WORKS

The objective of this study was to undertake a preliminary assessment of antimony levels in shallow soils within the assessment area from domestic surface soils and along roadways. The scope of works undertaken comprised:

 	Collection of a total of 91 soil samples including:

	66 shallow soil samples from exposed soil at 33 properties within the assessment area and 1 property outside the Costerfield area;

	10 deeper soil samples (up to 20 cm to 30 cm below ground level) at selected shallow soil locations;

and

	15 shallow soil samples were collected from roadways.

 	The preliminary assessment program was conducted in a manner consistent with the following:

	GoV (2002). State Environment Protection Policy (Prevention and Management of Contamination of Land). Victorian Government Gazette, No. S 95. Government of Victoria (GoV), June 2002.

	NEPC (2013).  Amended National Environment Protection Measure (Assessment of Site

Contamination) 1999. National Environment Protection Council (NEPC), May 2013.

	Australian Standard (AS) 4482.1-2005 (1997). Guide to the investigation and sampling of sites with potentially contaminated soil. Part 1: Non-volatile and semi-volatile compounds.

 	Assessment of analytical results against site specific screening levels developed during Department of Health (DHS) Personal Communication and Golder calculations consistent with the NEPC 2013.

Further detail on the methodology and assessment criteria is presented in Attachment A.

Golder Associates Pty Ltd

Building 7, Botanicca Corporate Park, 570 – 588 Swan Street, Richmond, Victoria 3121, Australia (PO Box 6079, Hawthorn West VIC 3122) Tel: +61 3 8862 3500  Fax: +61 3 8862 3501  www.golder.com

Golder Associates: Operations in Africa, Asia, Australasia, Europe, North America and South America

A.B.N. 64 006 107 857

Golder, Golder Associates and the GA globe design are trademarks of Golder Associates Corporation.

# 3.0	DATA QUALITY ASSURANCE AND QUALITY CONTROL

The field and laboratory procedures implemented for quality assurance/quality control (QA/QC) along with a discussion of the QA/QC results are presented in Attachment B.

Quality control samples collected as part of the sampling program included collection of field duplicates and field splits at a rate of at least 5 per cent, collection of rinsate blanks and container blanks. The laboratories implemented a Quality Control (QC) program including analysis of internal spikes, duplicates and method blanks.

Results for the overall QC completeness assessment are provided below in Table 2.

Table 1: Summary of QC Data Completeness

| QC Sample Type | Number of Results NOT Meeting Data Quality Objectives | Total Number of Results (Individual Analytes) | Percentage Meeting Data Quality Objectives |
| --- | --- | --- | --- |
| Primary Duplicates | 4 | 40 | 90% |
| Secondary Duplicates | 6 | 50 | 88% |
| Rinsates | 0 | 39 | 100% |
| Internal Duplicates | 1 | 117 | 99.1% |
| Matrix Spikes | 0 | 17 | 100% |
| Method Blanks | 0 | 55 | 100% |
| Overall Completeness | 11 | 318 | 96.5% |

Discussion on the completeness of each QC sample type is presented in Attachment C. The achieved overall completeness of 96.5% is above the overall completeness objective of 95%. Based on this outcome, Golder considers that the overall data quality generated during the assessment is of sufficient quality upon which to base decisions for this assessment.

# 4.0	RESULTS

A total of 91 samples were collected and submitted to ALS Environmental Laboratories for analysis. The analytical results have been tabulated and screened against guideline criteria. This data is presented in Table A.

As antimony is the main chemical of interest. A summary of the analytical results is presented in Table 1

below.

Table 2: Summary of antimony analytical results

| Sample Location | Sample depth | Number of samples | Range of reported results (mg/kg) | Adopted screening criterion | Number of samples exceeding adopted health screening level |
| --- | --- | --- | --- | --- | --- |
| Residential Properties | Surface scrape | 66 | <5 -4,230 | site specific criterion (200 mg/kg) | 17 |
|  | Subsurface | 10 | <5 - 2310 |  | 2 |
| Roads | Surface scrape | 15 | <5 - 3540 |  | 3 |
| TOTAL | 91 |  |  | 22 |

The preliminary assessment of antimony results collected from surface soils within the assessment area found:

 	Approximately one third of the reported antimony results are above the site specific health screening criterion.

 	Antimony levels exceeded site specific health screening criterion in at least one soil sample at 13 of the

34 properties sampled. The single property sampled outside the Costerfield area did not report

antimony levels above the site specific health screening criterion.

 	Antimony levels exceeded site specific health screening criterion at 3 of 15 roadways sampled.

# 5.0	LIMITATIONS

Your attention is drawn to the document - “Limitations”, which is included in Attachment C of this letter. The statements presented in this document are intended to advise you of what your realistic expectations of this report should be. The document is not intended to reduce the level of responsibility accepted by Golder, but rather to ensure that all parties who may rely on this report are aware of the responsibilities each assumes in so doing.

# 6.0	CLOSURE

If you have any questions please do not hesitate to contact the undersigned.

Yours sincerely

GOLDER ASSOCIATES PTY LTD

Nic Foot	Christian Wallis

Senior Environmental Engineer	Principal Environmental Scientist

NF/CJW/nf

CC:	The Government Reference Group

Attachments: Table A – Analytical Results

Attachment A – Sampling Methodology

Attachment B – Data Quality Assurance and Quality Control

Attachment C - Limitations

\\golder.gds\gap\melbourne\jobs\env\2014\147613051 - costerfield\correspondence out\147613051-004-l_soil factual report\147613051-004-l-rev0\01_147613051-004-l-rev0.docx

|  | Unknown | Exchangable Cations | Heavy Metals | Other | Sample Quality Parameters |
| --- | --- | --- | --- | --- | --- |
|  | pH Unit | % % % % | mg/kg mg/kg mg/kg mg/kg mg/kg | meq/kg | uS/cm mg/kg mg/kg % |
| LOR | 0.1 | 0.1 0.1 0.1 0.1 | 50 5 5 50 5 | 1 | 1 50 200 1 |
| NEPM 2013 HIL- Residential A Soil |  |  | 200 100 3800 |  |  |

| Property ID | Field_ID | Sampled_Date_Time | Sample_Point | Sample Description | SDG |
| --- | --- | --- | --- | --- | --- |
| 1 | 1/4001_20140603 | 3/06/2014 | surface | Clayey SILT, Brown, trace organics |  |
| 1 | 1/4002_20140603 | 3/06/2014 | surface | sandy SILT, dark brown, some organic matter |  |
| 2 | 2/4001_20140604 | 4/06/2014 | surface | silty CLAY, med plasticity, red-brwon, trace fine grained gravel |  |
| 2 | 2/4002_20140604 | 4/06/2014 | surface | silty CLAY, med plasticity, brown |  |
| 2 | 2/4003_20140604 | 4/06/2014 | subsurface | Silty CLAY, med-high plasticity, orange-brown |  |
| 3 | 3/4001_20140603 | 3/06/2014 | surface | Clayey SILT, Brown, trace organics |  |
| 3 | 3/4002_20140603 | 3/06/2014 | surface | Clayey SILT, Brown, trace organics and charcoal fragments |  |
| 4 | 4/4001_20140603 | 3/06/2014 | surface | clayey SILT, dark brown with some medium grained sand |  |
| 4 | 4/4002_20140603 | 3/06/2014 | surface | clayey SILT, brown, trace fine grained sand |  |
| 5 | 5/4001_20140603 | 3/06/2014 | surface | Clayey SILT. Brown, trace organics |  |
| 5 | 5/4002_20140603 | 3/06/2014 | surface | sandy SILT, dark brown, some organic matter |  |
| 6 | 6/4001_20140604 | 4/06/2014 | surface | sandy clayey SILT, brown, trace f-m grained gravel |  |
| 6 | 6/4002_20140604 | 4/06/2014 | surface | sandy clayey SILT, brown, trace f-m grained gravel |  |
| 7 | 7/4001_20140603 | 3/06/2014 | surface | sandy gravelly SILT |  |
| 7 | 7/4002_20140603 | 3/06/2014 | surface | silty sandy GRAVEL |  |
| 8 | 8/4001_20140603 | 3/06/2014 | surface | Clayey SILT, brown |  |
| 8 | 8/4002_20140603 | 3/06/2014 | surface | sandy SILT with some clay, dark brown, trace organics |  |
| 8 | 8/4003_20140603 | 3/06/2014 | subsurface | sandy SILT, brown with some clay |  |
| 9 | 9/4001_20140602 | 2/06/2014 | surface | sandy SILT, brown- black, fine to medium grained sand with trace organics |  |
| 9 | 9/4003_20140602 | 2/06/2014 | surface | sandy SILT, brown- black, fine to medium grained sand, some med grained angular gravel, with trace organics |  |
| 10 | 10/4001_20140604 | 4/06/2014 | surface | clayey SILT, brown, trace sand |  |
| 10 | 10/4002_20140604 | 4/06/2014 | surface | clayey SILT, brown, trace sand |  |
| 10 | 10/4003_20140604 | 4/06/2014 | subsurface | Clayey gravelly SILT, pale brown, fine-med grain gravel |  |
| 11 | 11/4001_20140605 | 5/06/2014 | surface | sandy SILT , brown, med grained sand, trace organics |  |
| 11 | 11/4002_20140605 | 5/06/2014 | surface | sandy SILT, dark brown, some organic matter |  |
| 12 | 12/4001_20140604 | 4/06/2014 | surface | gravelly SAND, dark brown, fine grained gravel with some silt |  |
| 12 | 12/4002_20140604 | 4/06/2014 | surface | sandy SILT with some clay, brown, med-grained sand |  |
| 13 | 13/4001_20140603 | 3/06/2014 | surface | clayey SILT, brown, with some organics |  |
| 13 | 13/4002_20140603 | 3/06/2014 | surface | clayey SILT, brown, with some organics |  |
| 14 | 14/4001_20140603 | 3/06/2014 | surface | sandy SILT, dark brown, high organic content |  |
| 14 | 14/4002_20140603 | 3/06/2014 | surface | clayey SILT, brown, some organic matter |  |
| 15 | 15/4001_20140604 | 4/06/2014 | surface | sandy SILT, dark brown, some fine grained gravel, trace clay |  |
| 15 | 15/4002_20140604 | 4/06/2014 | surface | sandy SILT, dark brown, trace clay and subrounded medium grained gravel |  |
| 16 | 16/4001_20140602 | 2/06/2014 | surface | sandy SILT, brown, fine grain sand, trace clay |  |
| 16 | 16/4002_20140602 | 2/06/2014 | surface | sandy SILT, brown, fine grain sand, trace clay |  |
| 18 | 18/4001_20140603 | 3/06/2014 | surface | sandy CLAY, brown, fine grain sand |  |
| 18 | 18/4002_20140603 | 3/06/2014 | surface | sandy SILT, brown, fine grained sand |  |
| 18 | 18/4003_20140603 | 3/06/2014 | subsurface | clayey SILT, pale brown |  |
| 20 | 20/4001_20140604 | 4/06/2014 | surface | clayey SILT, grey brown, trace organics |  |
| 20 | 20/4002_20140604 | 4/06/2014 | surface | clayey SILT, grey brown |  |
| 20 | 20/4003_20140604 | 4/06/2014 | subsurface | clayey SILT, grey brown |  |
| 21 | 21/4001_20140603 | 3/06/2014 | surface | sandy SILT, dark brown, coarse sand, some organic matter |  |
| 21 | 21/4002_20140603 | 3/06/2014 | surface | sandy SILT, dark brown, coarse sand, trace organic matter |  |
| 21 | 21/4003_20140603 | 3/06/2014 | subsurface | sandy SILT, dark brown, coarse sand |  |
| 22 | 22/4001_20140603 | 3/06/2014 | surface | silty SAND, coarse grained, dark brown, organics |  |
| 22 | 22/4002_20140603 | 3/06/2014 | surface | sandy SILT, brown, fine-med grain sand |  |
| 23 | 23/4001_20140605 | 5/06/2014 | surface | sandy SILT, dark brown, coarse sand |  |
| 23 | 23/4002_20140605 | 5/06/2014 | surface | clayey SILT, dark brown trace coarse grain sand |  |
| 24 | 24/4001_20140605 | 5/06/2014 | surface | clayey SILT, brown, fine - med grain gravels |  |
| 24 | 24/4002_20140605 | 5/06/2014 | surface | clayey SILT, brown, fine - med grain gravels |  |
| 26 | 26/4001_20140603 | 3/06/2014 | surface | clayey SILT, brown, trace organics |  |
| 26 | 26/4002_20140603 | 3/06/2014 | surface | clayey SILT, red brown, with gravel |  |
| 27 | 27/4001_20140604 | 4/06/2014 | surface | clayey SILT, brown, trace organics |  |
| 27 | 27/4002_20140604 | 4/06/2014 | subsurface | clayey SILT, brown |  |
| 27 | 27/4003_20140604 | 4/06/2014 | surface | clayey SILT, brown, trace organics |  |
| 27 | 27/4004_20140604 | 4/06/2014 | subsurface | clayey SILT, brown |  |
| 28 | 28/4001_20140604 | 4/06/2014 | surface | clayey SILT, dark brown, trace organics |  |
| 28 | 28/4002_20140604 | 4/06/2014 | surface | clayey SILT, brown, trace organics |  |
| 28 | 28/4003_20140604 | 4/06/2014 | subsurface | clayey SILT, brown, trace organics |  |
| 30 | 30/4001_20140605 | 5/06/2014 | surface | clayey SILT, brown, some fine-med grain gravel |  |
| 30 | 30/4002_20140605 | 5/06/2014 | surface | clayey SILT, dark brown, organics |  |
| 32 | 32/4001_20140605 | 5/06/2014 | surface | sandy SILT, brown, med grain sand, trace clay |  |
| 32 | 32/4002_20140605 | 5/06/2014 | surface | clayey gravelly SILT, brown, fine grain gravel |  |
| 32 | 32/4003_20140605 | 5/06/2014 | subsurface | clayey SILT, pale brown |  |
| 34 | 34/4001_20140605 | 5/06/2014 | surface | silty clayey SAND, brown, fine grain sand |  |
| 34 | 34/4002_20140605 | 5/06/2014 | surface | clayey Sandy SILT, dark brown, organic matter |  |
| 36 | 36/4001_20140602 | 2/06/2014 | surface | silty CLAY, dark red brown |  |
| 36 | 36/4002_20140602 | 2/06/2014 | surface | silty CLAY, dark brown |  |
| 37 | 37/4001_20140605 | 5/06/2014 | surface | snady clayey SILT, brown, fine -med grain sand |  |
| 37 | 37/4002_20140605 | 5/06/2014 | surface | snady clayey SILT, brown, fine -med grain sand with trace fine grain gravel |  |
| 40 | 40/4001_20140602 | 2/06/2014 | surface | sandy SILT, red brown, fine grain sand |  |
| 40 | 40/4002_20140602 | 2/06/2014 | surface | sandy SILT, red brown, fine grain sand with organics |  |
| 41 | 41/4001_20140604 | 4/06/2014 | surface | sandy SILT, dark brown, coarse grain sand, trace organics |  |
| 41 | 41/4002_20140604 | 4/06/2014 | surface | clayey SILT, orange brown |  |
| 42 | 42/4001_20140605 | 5/06/2014 | surface | clayey SILT, dark brown, trace medium grain sand, trace organics |  |
| 43 | 43/4001_20140605 | 5/06/2014 | surface | sandy SILT, pale brown, med grained sand, trace organics |  |
| R1 | R1/4001_20140605 | 5/06/2014 | roadway | sandy SILT, medium grained sand, pale brown, trace fine grained gravel |  |
| R10 | R10/4001_20140604 | 4/06/2014 | roadway | sandy SILT, dark and pale brown, trace fine grained gravel, trace clay |  |
| R11 | R11/4001_20140605 | 5/06/2014 | roadway | silty SAND, dark brown |  |
| R12 | R12/4001_20140604 | 4/06/2014 | roadway | silty, gravelly SAND, coarse sand, fine to medium grained gravel, brown |  |

|  | Unknown | Exchangable Cations | Heavy Metals | Other | Sample Quality Parameters |
| --- | --- | --- | --- | --- | --- |
|  | pH Unit | % % % % | mg/kg mg/kg mg/kg mg/kg mg/kg | meq/kg | uS/cm mg/kg mg/kg % |
| LOR | 0.1 | 0.1 0.1 0.1 0.1 | 50 5 5 50 5 | 1 | 1 50 200 1 |
| NEPM 2013 HIL- Residential A Soil |  |  | 200 100 3800 |  |  |

Property  ID	Field_ID	 Sampled_Date_Time	Sample_Point 	Sample Description 	SDG

| R13 R13/4001_20140604 4/06/2014 roadway gravelly SAND, coarse grained sand, fine to medium grained gravel, pale brown EM1405497 R14 R14/4001_20140605 5/06/2014 roadway silty SAND, coarse grained, pale yellow brown, trace fine grained gravel EM1405562 R15 R15/4001_20140605 5/06/2014 roadway sandy SILT, medium to coarse grained, dark brown, some fine gravel EM1405562 R2 R2/4001_20140605 5/06/2014 roadway silty SAND, coarse grained, pale yellow brown, trace fine grained gravel EM1405562 R3 R3/4001_20140605 5/06/2014 roadway sandy SILT, yellow brown, medium to coarse grained, trace fine to medium grained gravel EM1405562 R4 R4/4001_20140604 4/06/2014 roadway silty SAND, medium to coarse grained, angular, pale brown, some fine to medium grained gravel EM1405497 R5 R5/4001_20140605 5/06/2014 roadway sandy SILT, pale brown, medium grained sand, trace fine grained gravel EM1405562 R6 R6/4001_20140604 4/06/2014 roadway sandy SILT, dark brown, trace fine grained gravel, trace clay EM1405497 R7 R7/4001_20140604 4/06/2014 roadway sandy SILT, brown, some fine grained gravel, trace clay EM1405497 R8 R8/4001_20140604 4/06/2014 roadway sandy SILT, dark brown, fine to medium grained sand, trace organic matter EM1405497 R9 R9/4001_20140604 4/06/2014 roadway clayey SILT, dark and pale brown, trace fine grained gravel EM1405497 | 6.6 7.8 5.8 6.8 6.3 6.5 7.2 7.5 7 6 6.4 | - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - | 2,380 <5 <5 6,040 34 4,870 <5 <5 38,200 282 4,670 43 <5 28,900 219 3,540 14 <5 5,110 32 8,800 22 10 35,800 112 6,370 <5 <5 13,200 76 3,720 1,330 48 37,100 232 4,440 9 <5 35,500 334 5,690 124 44 48,800 143 9,260 229 13 34,500 381 7,550 108 8 34,400 312 | - - - - - - - - - - - | 11 - - 5.3 47 - - 12.4 21 - - 17.6 58 - - 11.8 20 - - 18.8 16 - - 9.9 180 - - 15.2 74 - - 7.8 245 - - 12.6 72 - - 42.7 95 - - 38.5 |
| --- | --- | --- | --- | --- | --- |

Statistical Summary

| Number of Results Number of Detects Minimum Concentration Minimum Detect Maximum Concentration Maximum Detect Average Concentration Median Concentration Standard Deviation Number of Guideline Exceedances Number of Guideline Exceedances(Detects Only) | 91 91 3.9 3.9 7.8 7.8 5.6 5.5 0.96 0 0 | 2 2 2 2 2 2 2 0 2.2 1.2 0.4 <0.1 2.2 1.2 0.4 ND 9.2 1.8 0.6 <0.1 9.2 1.8 0.6 ND 5.7 1.5 0.5 0.05 0 0 0 0 0 0 0 0 | 91 91 91 91 91 91 81 74 91 91 1280 <5 <5 3030 16 1280 8 5 3030 16 22300 4230 367 82500 1650 22300 4230 367 82500 1650 6355 340 32 25240 260 5690 80 12 22500 197 3127 739 55 16848 268 0 22 8 0 0 0 22 8 0 0 | 2 2 38 38 115 115 76.5 0 0 | 91 14 2 91 91 2 2 91 4 <50 31800 5.3 4 60 31800 5.3 1390 250 46700 49.9 1390 250 46700 49.9 86 44 24 38 25 39250 20.4 164 60 12 0 0 0 0 0 0 0 0 |
| --- | --- | --- | --- | --- | --- |

ATTACHMENT A

Sampling Methodology

| Item | Description |
| --- | --- |
| Sample Date | 2, 3, 4 and 5 June 2014. The following weather observations were made during the sampling event:  2 June 2014 – overcast  3 June 2014 – overcast, light showers in the morning  4 June 2014 – foggy in the morning, sunny afternoon  5 June 2014 – overcast (ground conditions very wet from overnight rain) |
| Adopted Sampling Guidelines |  Australian/New Zealand Standard 4482.1 (2005) Guide to the investigation and sampling of sites with potentially contaminated soil. Part 1: Non-volatile and semi-volatile compounds. This standard was prepared as part of a series on the identification, analytical methods and investigation procedures for the assessment of soil. The objective of this standard is to derive the information which may be required to satisfy regulatory authorities, although additional detail may be required in some locations.  National Environment Protection (Assessment of Site Contamination) Amendment Measure 2013 (No.1). This guidance is recognised as the primary national guidance document for the assessment of site contamination in Australia. The purpose of the guideline is to ‘establish a nationally consistent approach to the assessment of site contamination to ensure sound environmental management practices by the community which includes regulators, site assessors, environmental auditors, landowners, developers and industry’. |
| Sample Points |  Surface samples: Exposed soil near main dwelling on accessed properties.  Subsurface samples: Subsurface soil within assessment area, samples collected 20 cm below the ground surface with one exception where sample was collected 10 cm below the ground surface (a deeper sample was not able to be collected due to hard ground conditions).  Roadway samples: Exposed soil on dirt roadways within the assessment area. |
| Number of Primary Soil Samples Collected |  Surface samples – 66 samples  Subsurface samples – 10 samples  Roadway samples – 15 samples |
| Soil collection methodology |  Surface and Roadway samples: To represent exposed soil, the ground surface was gently scraped with either by a gloved hand or clean trowel to collect surface soil.  Subsurface samples: A hole was dug to half the required depth using a clean shovel. A clean trowel was then used to excavate to required depth. Sample was collected using the trowel and/or gloved hands. |

| Item | Description |
| --- | --- |
|  |  Trowels and shovels were decontaminated between each soil sampling location by first removing any soil adhered to the trowel and shovel, washing the equipment in a bucket with phosphate-free detergent using brushes then rinsed in another bucket of laboratory supplied de-ionised water.  Nitrile gloves were replaced between each soil sampling location. |
| Record of Sample Location | Sampling locations were recorded with hand-held GPS with +/- 10 m accuracy. |
| Sample Storage | Soil samples were placed in new jars supplied by the laboratory, jars were labelled with a unique identifier. |
| Sample Delivery | The samples were transferred into chilled, insulated containers and delivered to the laboratory under Chain of Custody (CoC) procedures. |
| Laboratory for Soil Analysis | The laboratory engaged as the primary laboratory for the analysis was ALS Environmental Pty Ltd which is registered by the National Association of Testing Authority (NATA) for the analyses performed. The secondary laboratory selected for quality assurance testing was MGT Eurofins. |
| Laboratory Analytical Schedule | Selected samples were designated for analysis of soil pH, electrical conductivity and metals (including antimony, arsenic, aluminium, iron and manganese). Sulphate, total organic carbon (TOC) and cation exchange capacity (CEC) were also analysed for selected samples. At the time of reporting, the analysis had not been reported. |
| Adopted Assessment Criteria |  National Environment Protection (Assessment of Site Contamination) Measure (NEPM), 2013 Health Investigation Levels - Residential A Soil (HIL A). ‘Residential A’ soil represents that in areas of low density residential land.  The soil screening criteria were selected based on the objectives of the State Environment Protection Policy (Prevention and Management of Contamination of Land) (Land SEPP).The soil assessment criteria adopted for the protected beneficial use of ‘Human Health’ in low density residential areas is the NEPM 2013 HIL A. Other beneficial uses of land are not considered in this assessment.  It is noted that an exceedance of the adopted human health criteria does not necessarily indicate an unacceptable risk to human health in relation to the respective land use scenario. Rather, an exceedance would trigger the need for further assessment to understand the risk (under the amended NEPM 2013) and possibly the need for a site-specific human health risk assessment which would evaluate the relevant exposure setting and associated risks.  Victorian Department of Human Services Personal Correspondence Tuesday 10 June 2014 detailed a residential oil guideline of 100-300mg/kh for antimony when people are exposed via soil and drinking water. The recently adopted NEPM (2013) includes a calculator for estimating HIL values for substances. Using the tolerable daily intake of 0.006mg/kg the calculated value is 200mg/kg. |

ATTACHMENT B

Data Quality Assurance and Quality Control

Item	Description

QA/QC Objectives

Data Quality Measures and Objectives

The data quality measures for the assessment are as follows:

    Accuracy: A measure of the closeness of the results to the actual results.

Accuracy is assessed through the comparison of results produced by the

primary  and  secondary  laboratories  for  the  same  sample  and  by  the measuring of the extent to which an analytical result reflects the known concentration as measured by the recovery obtained from internal laboratory spikes.

 	Precision: A measure of the repeatability of results by the laboratory. This is assessed through the analysis of duplicates both internally and externally.

 	Completeness: The percentage of acceptable data obtained compared to the amount of data needed to achieve a particular level of confidence in the

results.

The following data quality objectives (DQOs) have been set for this project:

    primary   samples   and   field   duplicates   recording   Relative   Percentage

Differences  (RPDs)  less  than  30%  for  inorganics  and  less  than  50%  for

organics;

 	primary samples and primary laboratory internal duplicates recording RPDs less than 30% for inorganics and less than 50% for organics;

 	accuracy in spike samples to range between 70% and 130% (for organics and other inorganics);

 	rinsate   blanks   and   primary   laboratory   method   blanks   below   practical quantitation limits (PQLs), or equal or less than background levels, wherever

justified;

    overall data quality completeness of 95% or greater.

The primary and secondary duplicate results for chemical data were compared with primary  sample  results  using  RPDs.  RPDs  were  calculated  according  to  the following formula:

% RPD  ABS  A  B   200 

		

 A  B 	

Where:	ABS – absolute number

A – concentration of the primary laboratory result per analyte

B – concentration of corresponding duplicate result.

RPD values can range from 0% (indicating perfect correlation between results) to

200% (indicating complete divergence in results).

Item	Description

QA/QC Methodology

| QA/QC Sample Collection | The following QA/QC samples were collected:  Primary and secondary duplicate samples at a frequency of 5.4% against primary samples.  Three rinsate samples collected off of reusable trowel; one sample for each of the three days the trowel was used in soil collection. |
| --- | --- |
| Minimisation of cross-contamination | Golder staff used new nitrile gloves for collection of each soil sample and decontaminated reusable equipment between each location. |
| Sample Handling and Preservation | Soil samples were collected into laboratory supplied jars with appropriate Polytetrafluoroethylene lined lids. The collected samples were immediately placed in a chilled and insulated container with ice and stored in this manner prior to and during transit to the laboratory. |
| Laboratory Internal QC | The quality of the laboratory data generated was supported with appropriate laboratory Quality Control (QC) samples and assessed using standard methods. Internal laboratory QC samples including method blanks, laboratory duplicates, matrix spikes, laboratory control sample spikes and surrogate spikes were analysed as part of the quality assurance program. |

QA/QC Results

| Summary of Water QA/QC Results |  |
| --- | --- |
|  | QC Sample Type | Number of Results NOT Meeting Data Quality Objectives | Total Number of Results (Individual Analytes) | Percentage Meeting Data Quality Objectives |
|  | Primary Duplicates | 4 | 40 | 90% |
|  | Secondary Duplicates | 6 | 50 | 88% |
|  | Rinsates | 0 | 39 | 100% |
|  | Internal Duplicates | 1 | 117 | 99.1% |
|  | Matrix Spikes | 0 | 17 | 100% |
|  | Method Blanks | 0 | 55 | 100% |
|  | Overall Completeness | 11 | 318 | 96.5% |
| Discussion of Results |  Five primary and five secondary duplicate samples were analysed during the assessment and a total 93 primary soil samples analysed. This equates to an analysis frequency of 5.4% for collection duplicate samples. This complies with the specified collection rate of 5%. Primary and secondary analytical results are presented in Table B-1 at the back of this attachment.  Of the 40 primary duplicate analytes, four returned RPDs above 50%, representing a non-conformance level of 90%. The non-conformances were |

Item	Description

observed for one each for aluminium (RPD of 57), arsenic (RPD of 79), antimony (RPD of 50) and iron (RPD of 61).

 	Of  the  50  secondary  duplicate  analytes,  6  returned  RPDs  above  50%, representing a non-conformance level of 88%. Non-conformances, with RPDs

ranging between 51 and 134, were observed for electrical conductivity (one result, RPD of 52) and metals including arsenic (three results, RPDs of 57,

111 and 117), antimony (one result, RPD of 134), manganese (one result, RPD of 127).

 	The non-conformances observed in both primary and secondary duplicates are likely due to the heterogeneous nature of the surface soil and difficulties

obtaining true duplicates from the field splitting process. Due to an objective of taking only a surface sample, a large area of exposed soil was required for collecting  duplicate  samples. Primary  and  secondary  analytical  results  are presented in Table B-1 at the back of this attachment. It is considered unlikely that the non-conformance will affect the overall quality or outcome of the assessment.

 	None of the 39 rinsate analysis results reported levels above the laboratory limit of reporting. This represents compliance of 100%.

 	A review of the RPDs for the Internal duplicate tests indicates that 1 of the 117 tests  conducted  did  not  produce  results  within  the  desired  30%  RPD

conformance limit. This result represents a compliance of 99.1%.   It is considered unlikely that the non-conformance will affect the overall quality or outcome of the assessment.

 	A review of the 17 Matrix Spike results indicates that all analyses provided a recovery beyond 70-130%, representing a conformance level of 100%.

 		A review of the Method Blank tests indicates that all of the 55 laboratory internal blanks analytes were below laboratory reporting limit, representing

compliance of 100%.

The achieved QA/QC completeness of 95.9% is above the overall completeness objective of 95%. Based on this outcome, it is considered that the overall data quality generated during the assessment of water by Golder is of sufficient quality upon which to base decisions for this assessment.

\\golder.gds\gap\melbourne\jobs\env\2014\147613051 - costerfield\correspondence out\147613051-004-l_soil factual report\147613051-004-l-rev0\04_attachment b qaqc_soil docx_cjw.docx

Primary Duplicates

Table B-1: Primary and Secondary Duplicate Analytical Results	Soil Monitoring

Costerfield

147613051

*RPDs have only been considered where a concentration is greater than 0 times the EQL

**High RPDs are in bold (Acceptable RPDs for each EQL multiplier range are: 50 (0-10 x EQL); 50 (10-30 x EQL); 50 ( > 30 x EQL)

***Interlab Duplicates are matched on a per compound  basis as methods vary between  laboratories.   Any methods in the row header relate to those used in the primary laborator

Secondary  Duplicates

*RPDs have only been considered where a concentration is greater than 0 times the EQL

**High RPDs are in bold (Acceptable RPDs for each EQL multiplier range are: 50 (0-10 x EQL); 50 (10-30 x EQL); 50 ( > 30 x EQL)

***Interlab Duplicates are matched on a per compound  basis as methods vary between  laboratories.   Any methods in the row header relate to those used in the primary laborator

Secondary  Duplicates

| Chem_Group | ChemName | Units | EQL |  |  |
| --- | --- | --- | --- | --- | --- |
| Heavy Metals | Aluminium | mg/kg | 50 : 10 (Interlab) 9970 | 13000 | 26 |
|  | Antimony | mg/kg | 5 : 10 (Interlab) 18 | 91 | 134 |
|  | Arsenic | mg/kg | 5 : 2 (Interlab) 7 | <2 | 111 |
|  | Iron | mg/kg | 50 : 5 (Interlab) 31200 | 33000 | 6 |
|  | Manganese | mg/kg | 5 304 | 68 | 127 |
| Sample Quality Parameters | Electrical Conductivity @ 25°C | uS/cm | 1 : 10 (Interlab) 10 | <10 | 0 |
|  | Moisture | % | 1 : 0.1 (Interlab) 12.7 | 11 | 14 |
| Unknown | PH_CACL2 | pH Unit | 0.1 |  |  |

*RPDs have only been considered where a concentration is greater than 0 times the EQL

**High RPDs are in bold (Acceptable RPDs for each EQL multiplier range are: 50 (0-10 x EQL); 50 (10-30 x EQL); 50 ( > 30 x EQL)

***Interlab Duplicates are matched on a per compound  basis as methods vary between  laboratories.   Any methods in the row header relate to those used in the primary laborator

13/06/2014	Page 1 of 1

ATTACHMENT C

Limitations

16 June 2014

Report No. 147613051-004-L-Rev0

# LIMITATIONS

This Document has been provided by Golder Associates Pty Ltd (“Golder”)

subject to the following limitations:

This  Document  has  been  prepared  for  the  particular  purpose  outlined  in Golder’s  proposal  and  no  responsibility  is  accepted  for  the  use  of  this Document, in whole or in part, in other contexts or for any other purpose.

The scope and the period of Golder’s Services are as described in Golder’s proposal, and are subject to restrictions and limitations.  Golder did not perform a complete assessment of all possible conditions or circumstances that may exist at the site referenced in the Document.  If a service is not expressly indicated, do not assume it has been provided.  If a matter is not addressed, do not assume that any determination has been made by Golder in regards to it.

Conditions may exist which were undetectable given the limited nature of the enquiry Golder was retained to undertake with respect to the site.  Variations in conditions may occur between investigatory locations, and there may be special conditions pertaining to the site which have not been revealed by the investigation and which have not therefore been taken into account in the Document. Accordingly, additional studies and actions may be required.

In addition, it is recognised that the passage of time affects the information and assessment provided in this Document.  Golder’s opinions are based upon information that existed at the time of the production of the Document.   It is understood that the Services provided allowed Golder to form no more than an opinion of the actual conditions of the site at the time the site was visited and cannot be used to assess the effect of any subsequent changes in the quality of the site, or its surroundings, or any laws or regulations.

Any assessments made in this Document are based on the conditions indicated from  published  sources  and  the  investigation  described.  No  warranty  is included, either express or  implied, that  the actual conditions will conform exactly to the assessments contained in this Document.

Where data supplied by the client or other external sources, including previous site  investigation  data,  have  been  used,  it  has  been  assumed  that  the information is correct unless otherwise stated. No responsibility is accepted by Golder for incomplete or inaccurate data supplied by others.

Golder may have retained subconsultants affiliated with Golder to provide Services for the benefit of Golder.  To the maximum extent allowed by law, the Client acknowledges and agrees it will not have any direct legal recourse to, and waives any claim, demand, or cause of action against, Golder’s affiliated companies, and their employees, officers and directors.

This Document is provided for sole use by the Client and is confidential to it and its professional advisers. No responsibility whatsoever for the contents of this Document will be accepted to any person other than the Client.  Any use which a third party makes of this Document, or any reliance on or decisions to be made based on it, is the responsibility of such third parties.  Golder accepts no responsibility for damages, if any, suffered by any third party as a result of decisions made or actions based on this Document.

GOLDER ASSOCIATES  PTY LTD	GAP Form No.  LEG 04  RL 1

APPENDIX C

Interim Air Monitoring – Laboratory Report

17 June 2014

Report No. 147613051-001-R-Rev1

13 May 2014

Project No. 147613051-005-L-Rev0

John Mitas

Department of State Development, Business and Innovation

Level 9, 121 Exhibition Street

Melbourne  VIC 3000

# INTERIM AIR MONITORING: LABORATORY REPORT ONE

Dear John,

Golder Associates (Golder) was commissioned by the Department of State Development, Business and Innovation (DSDBI) to undertake interim air quality monitoring at one location in the vicinity of Mandalay Resources gold-antimony operation at Costerfield, Victoria.

The interim monitoring programme scope is summarised in Table 1.

Table 1: Interim Monitoring Programme Scope

| Atmospheric Contaminant | Sample Duration | Sample Frequency |
| --- | --- | --- |
| A PM10 | 24 hours | One every two days |
| B Particulate metal, measured in the PM10 fraction | 24 hours | One every two days |
| PM C 2.5 | 24 hours | One every two days |
| Indicative PM10 | Continuous | Continuous |
| Deposited dust (insoluble solids) | Two weeks | Continuous |
| Deposited dust (particulate metals)B | Two weeks | Continuous |

NOTES

A	Particulate matter with an equivalent aerodynamic diameter (EAD) less than 10 microns (PM10)

B	Arsenic, barium, beryllium, cadmium, cobalt, chromium, manganese, nickel, lead, antimony, vanadium, zinc

C	Particulate matter with an EAD less than 2.5 microns (PM2.5)

The following laboratory report outlines the results from the period 3 June 2014 to 9 June 2014.

The laboratory report is issued in accordance with Golder’s National Association of Testing Authorities (NATA) laboratory accreditation, 1910. The results of the tests included in this document are traceable to Australian/national standards. Golder is accredited for compliance with ISO/IEC 17025.

Golder Associates Pty Ltd

Building 7, Botanicca Corporate Park, 570 – 588 Swan Street, Richmond, Victoria 3121, Australia (PO Box 6079, Hawthorn West VIC 3122) Tel: +61 3 8862 3500 Fax: +61 3 8862 3501 www.golder.com

Golder Associates: Operations in Africa, Asia, Australasia, Europe, North America and South America

A.B.N. 64 006 107 857

Golder, Golder Associates and the GA globe design are trademarks of Golder Associates Corporation.

# 1.0	TEST METHODS

## 1.1	PM10

Ambient air was drawn at a constant flowrate through a size selective inlet and pre-weighed quartz filter using a High Volume Sampler (HVS). PM10 is separated from suspended matter by the size selective inlet and collected on the filter media.

Filter samples were allowed to equilibrate in a temperature and humidity controlled environment before gravimetric analysis.

The weight change of the quartz filter was determined using a Mettler Toledo four figure balance. Control filters were used to check for changes in environmental conditions between weight determinations.

The Mettler Toledo balance was calibrated to comply with NATA specifications (NATA Calibration Report No. BE156143, 26 May 2014).

The method used was in accordance with Golder Test Method H3: High Volume Sampler (HVS) Operation

TSP, PM10 and PM2.5 Determination – In Ambient Air, based on Australian Standard AS/NZS 3580.9.6

Methods for Sampling and Analysis of Ambient Air. Method 9.6: Determination of Suspended Particulate

Matter – PM10 High Volume Sampler with Size Selective Inlet – Gravimetric Method.

### 1.1.1	Particulate Metals (PM10 Fraction)

Following gravimetric analysis filter samples were analysed by Inductively Coupled Plasma Mass Spectrometry (ICP-MS) to determine the metals content. Sample analysis was conducted by ALS Sydney, NATA Accreditation No. 825.

## 1.2	PM2.5

Ambient air was drawn at a constant flowrate through a size selective inlet and pre-weighed filter using a High Volume Sampler (HVS). PM2.5 is separated from suspended matter by the size selective inlet and collected on the filter media.

Filter samples were allowed to equilibrate in a temperature and humidity controlled environment before gravimetric analysis.

The weight change of the filter was determined using a Mettler Toledo four figure balance. Control filters were used to check for changes in environmental conditions between weight determinations.

The Mettler Toledo balance was calibrated to comply with NATA specifications (NATA Calibration Report No. BE156143, 26 May 2014).

The method used was in accordance with Golder Test Method H3: High Volume Sampler (HVS) Operation

TSP, PM10 and PM2.5 Determination – In Ambient Air, based on Australian Standard AS/NZS 3580.9.14

Methods for Sampling and Analysis of Ambient Air. Method 9.14: Determination of Suspended Particulate

Matter – PM2.5 High Volume Sampler with Size Selective Inlet – Gravimetric Method.

## 1.3	Indicative PM10

Indicative PM10 monitoring was conducting using a continuous laser light scattering instrument co-located with the HVS. The measurement technique is not an Australian Standard method, however the indicative results provide a measure of PM10 trends and variation during collection of the discrete HVS filter samples.

The instrument was calibrated prior to use and maintenance checks were conducted on a regular basis. NATA accreditation does not cover indicative instruments.

## 1.4	Deposited Dust (Insoluble Solids and Metals)

Particles settling from the air are collected in a vessel and contained with any rainwater from the sample period. Sample analysis involves sieving to remove extraneous matter followed by filtration and drying. Insoluble solids content is determined gravimetrically. Metals content is determined by ICP-MS.

# 2.0	MEASUREMENT UNCERTAINTY

## 2.1	PM10

AS3580.9.6 estimates the method precision as typically 5 µg/m3 over the measurement range.

### 2.1.1	Particulate Metals (PM10 Fraction)

The analytical laboratory has not reported a measurement uncertainty for metals determination from HVS

filters.

## 2.2	PM2.5

The estimated measurement uncertainty for PM2.5 by HVS is ± 5 µg/m

## 2.3	Deposited Dust (Insoluble Solids)

over the measurement range.

The estimated measurement uncertainty for deposited dust (insoluble solids) is ± 0.3 g/m2/month, at a 95%

confidence interval, calculated using a coverage factor of 1.96.

### 2.3.1	Deposited Dust (Particulate Metals)

The analytical laboratory has not reported a measurement uncertainty for metals determination from dust deposit gauge samples.

# 3.0	MONITORING LOCATION

The interim air monitoring location is established at a neighbourhood location in a paddock adjacent to the Heathcote-North Costerfield Road. The location is approximately one kilometre north of the Mandalay Resources Brunswick Plant.

Monitoring location details are presented in Table 2.

Table 2: Monitoring Location Details

| Element | Monitoring Location |
| --- | --- |
| Classification of Area | Neighbourhood |
| UTM Co-ordinates (m) | 302 949 E, 5916 610 S (UTM Zone 55) |
| Elevation (m) | 202 |
| Description | The monitoring location is located in a grassed paddock, approximately 20 m from the nearest building. |
| Distance from Mandalay Resources | Approximately 1 km |
| Direction from Mandalay Resources | Approximately north |
| Extraneous sources | Approximately 90 m from an unsealed road |

The monitoring location was selected with consideration of the requirements of Australian Standard AS/NZS

3580.1.1 Methods for Sampling and Analysis of Ambient Air. Part 1.1: Guide to Siting Air Monitoring

Equipment. An assessment of compliance with the Standard requirements is presented in Table 3.

Table 3: Monitoring Location Compliance Assessment

| AS/NZS 3580.1.1 Requirement | Monitoring Location Status |
| --- | --- |
|  | PM10, PM10 Metals and PM2.5 | Deposited Dust |
| Height above ground to sampling inlet 1.0 – 5 m | OK | Not applicable |
| Height above ground to sampling inlet 2.0 ±0.2 m | Not applicable | OK |
| Clear sky angle 120° | OK | OK |
| Unrestricted airflow of 270° | OK | Not applicable |
| Unrestricted airflow of 360° | Not applicable | OK |
| 10 m from the nearest object or dripline of trees that are higher than 2 m below the height of the sample inlet. | OK | OK |
| No extraneous sources nearby | OK | OK |
| Greater than 50 m from road | OK | Not applicable |

# 4.0      RESULTS

The interim monitoring programme results are presented in Table 4 and Table 5. Indicative PM10 results are presented in Figure 1 with summary statistics presented in Table 6. Deposited dust results are not available for the monitoring period.

Table 4: PM10 and PM10 Metals Results

Concentration Results (µg/m3)C

| D PM10 | 8.9 | 6.9 | 8.9 |
| --- | --- | --- | --- |
| ArsenicE | <0.0005 | <0.0004 | 0.00032 |
| BariumE | <0.003 | <0.002 | <0.002 |
| BerylliumE | <0.0005 | <0.0004 | <0.0004 |
| CadmiumE | <0.0005 | <0.0004 | <0.0004 |
| CobaltE | <0.0005 | <0.0004 | <0.0004 |
| ChromiumE | <0.003 | <0.002 | <0.002 |
| ManganeseE | <0.0009 | 0.0019 | 0.00070 |
| NickelE | <0.0007 | 0.00045 | <0.0005 |
| LeadE | <0.002 | 0.0012 | 0.00089 |
| AntimonyE | 0.011 | 0.011 | 0.0054 |
| VanadiumE | <0.004 | <0.003 | <0.003 |
| ZincE | <0.05 | <0.03 | <0.03 |

NOTES

A	Eastern standard time

B	Sample period was less than the recommended period of 24 hours ± 1 hour due to a power interruption

C	Concentration corrected to 0°C and 101.3 kPa

D	Sample analysis conducted by Golder, NATA Accreditation Number 1910

E	Sample analysis conducted by ALS Sydney, NATA Accreditation Number 825.  Laboratory Report Number ES1412728.

Table 5: PM2.5 Results

Concentration Results (µg/m3)C

| PM2.5 | 2.6 | 2.5 | 2.8 |
| --- | --- | --- | --- |

NOTES

A	Eastern standard time

B	Sample period was less than the recommended period of 24 hours ± 1 hour due to a power interruption

C	Concentration corrected to 0°C and 101.3 kPa. Sample analysis conducted by Golder, NATA Accreditation Number 1910.

120

100

80

60

40

Power

Interuption

20

0

Figure 1: Indicative PM10 Results

Table 6: Indicative PM10 Summary Statistics

| Date | 3/06/2014 | 4/06/2014 | 5/06/2014 | 6/06/2014 | 7/06/2014 | 8/06/2014 | 9/06/2014 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Start TimeA | 00:00 | 00:00 | 00:00 | 00:00 | 00:00 | 00:00 | 0.00 |
| End TimeA | 23:59 | 23:59 | 23:59 | 23:59 | 23:59 | 23:59 | 23:59 |
| Minimum (µg/m3)B | 6 | 6 | 2 | 2 | 3 | 4 | 1 |
| Average (µg/m3)B | 11 | 12 | 9 | 9 | 10 | 8 | 7 |
| Maximum (µg/m3)B | 24 | 112 | 20 | 19 | 27 | 15 | 17 |

NOTES

A	Eastern standard time

B	Summary statistics are calculated from 1 minute averages.

# 5.0	CLOSURE

Please contact the undersigned if you have any questions regarding this laboratory report. Yours sincerely,

GOLDER ASSOCIATES PTY LTD

Jacinda Shen

Associate - Air Quality Specialist

JSHEN/MT/jshen

Attachments: Limitations ‘GAP Form No. LEG04’

j:\env\2014\147613051 - costerfield\correspondence out\147613051-005-l-air laboratory report 1\147613051-005-l-rev0-interim air monitoring-laboratory report one.docx

# LIMITATIONS

This Document has been provided by Golder Associates Pty Ltd (“Golder”)

subject to the following limitations:

This  Document  has  been  prepared  for  the  particular  purpose  outlined  in Golder’s  proposal  and  no  responsibility  is  accepted  for  the  use  of  this Document, in whole or in part, in other contexts or for any other purpose.

The scope and the period of Golder’s Services are as described in Golder’s proposal, and are subject to restrictions and limitations.  Golder did not perform a complete assessment of all possible conditions or circumstances that may exist at the site referenced in the Document.  If a service is not expressly indicated, do not assume it has been provided.  If a matter is not addressed, do not assume that any determination has been made by Golder in regards to it.

Conditions may exist which were undetectable given the limited nature of the enquiry Golder was retained to undertake with respect to the site.  Variations in conditions may occur between investigatory locations, and there may be special conditions pertaining to the site which have not been revealed by the investigation and which have not therefore been taken into account in the Document. Accordingly, additional studies and actions may be required.

In addition, it is recognised that the passage of time affects the information and assessment provided in this Document.  Golder’s opinions are based upon information that existed at the time of the production of the Document.   It is understood that the Services provided allowed Golder to form no more than an opinion of the actual conditions of the site at the time the site was visited and cannot be used to assess the effect of any subsequent changes in the quality of the site, or its surroundings, or any laws or regulations.

Any assessments made in this Document are based on the conditions indicated from  published  sources  and  the  investigation  described.  No  warranty  is included, either express or  implied, that  the actual conditions will conform exactly to the assessments contained in this Document.

Where data supplied by the client or other external sources, including previous site  investigation  data,  have  been  used,  it  has  been  assumed  that  the information is correct unless otherwise stated. No responsibility is accepted by Golder for incomplete or inaccurate data supplied by others.

Golder may have retained subconsultants affiliated with Golder to provide Services for the benefit of Golder.  To the maximum extent allowed by law, the Client acknowledges and agrees it will not have any direct legal recourse to, and waives any claim, demand, or cause of action against, Golder’s affiliated companies, and their employees, officers and directors.

This Document is provided for sole use by the Client and is confidential to it and its professional advisers. No responsibility whatsoever for the contents of this Document will be accepted to any person other than the Client.  Any use which a third party makes of this Document, or any reliance on or decisions to be made based on it, is the responsibility of such third parties.  Golder accepts no responsibility for damages, if any, suffered by any third party as a result of decisions made or actions based on this Document.

GOLDER ASSOCIATES  PTY LTD	GAP Form No.  LEG 04  RL 1

APPENDIX D

Copy of Department of Health Community Fact Sheet for

Antimony May 2014

17 June 2014

Report No. 147613051-001-R-Rev1

Community fact sheet                         May 2014

# What is antimony?

Antimony is a brittle silver-white metal that occurs in soil and rocks in certain parts of the world. It is not found very often or in large amounts, however it enters the environment during the mining or processing of its ores and in the production of antimony metal, alloys and combinations of this metal with other substances.

# How is antimony used?

Antimony and its compounds are used to make a variety of products such as:

•	Metal alloys where it imparts hardness, strength, anticorrosion and other properties

•	Flame retardant treatments for textiles, plastics, rubber and some building materials

•	Consumer products including electrical devices, paints, plastics and pottery.

•	In some medicines for treating parasitic diseases (usually in animals). Historically, antimony was once used in medicine to induce vomiting.

# Where is antimony found in the general environment?

In soils: Some soils have naturally high levels of antimony. Antimony generally binds strongly to soil particles.

In mine tailings:  Antimony is sometimes found in rock containing gold.  Gold mining activities bring the rock to the surface where it has been crushed to extract the gold.  The leftover crushed rock, known as mine tailings can contain antimony.

In creeks and rivers: Antimony may occur in creeks or rivers where there are high levels of antimony in soil or rocks. Antimony does not appear to accumulate in fish or other aquatic animals. It also does not dissolve well in water and remains attached to particles of dirt.

In air:  Airborne dust from metal smelting operations and some dusts in the workplace can have high levels of antimony. Dust from mine tailings and certain soils generally have much lower levels of antimony.

Mining of natural deposits of antimony occurs in a few locations in Australia, In Costerfield, in central Victoria, antimony has been mined with gold at different times since the 1860s. Today, the mine is operated by the company, Mandalay Resources.

# How are people exposed to antimony?

As antimony is naturally occurring in the environment, people are exposed to relatively small amounts every day in air, food and water. Most of the antimony in your body comes from food and drinking water. In comparison, small amounts may also come from exposure to dust or soil.

Most antimony taken into the body through the diet leaves the body in the urine or faeces within a few days. Antimony in dust or soil is bound to soil particles, therefore is not well absorbed by the body if swallowed.  It is not known whether antimony can be absorbed into the body through the skin.

# What levels of antimony exposure are known to affect health?

Most of the studies into the health effects of antimony exposure have looked at worker exposure to high levels of antimony in air, or in people who have swallowed a large dose of medication containing antimony.

In workers:  Exposure to high levels in air for a long time can cause irritation to the skin and eyes as well as coughing. Breathing in 2 mg/m3 (antimony in air) over a long time can cause problems  with the lungs (pneumoconiosis); heart problems (high blood pressure, irregular heartbeat); stomach pain, diarrhoea, vomiting

and possible reproductive problems. There is insufficient evidence to classify  antimony as a human cancer­

causing agent.

In medicines:  Swallowing a single, high dose of antimony (ie 30 milligrams) can cause nausea and vomiting. Vomiting reduces the amount of antimony taken up by the body.

# What levels of antimony in the environment  are safe?

The following information is relevant to general population exposures to antimony.

Total daily intake over a lifetime:     The World Health Organization has calculated a safe level of antimony that a person can take into the body every day over a lifetime.  This value has been determined from studies in animals with conservative safety factors applied to protect human health.  This acceptable daily intake  is 6

microgram/kg body weighUday1.

An adult weighing 70 kg can take into their body 420 micrograms of antimony per day without effect. A one year old child weighing 1Okg can take into their body 60 micrograms of antimony per day without effect.

Drinking water:    The Australian Drinking Water Guideline (ADWG) value for antimony is 3 micrograms/L.

Soils: There is no Australian Guideline level for antimony in soil.

# What can you do if you live in a high antimony area?

Drinking water:

If you have access to a reticulated drinking water supply, use this water for drinking and cooking.

In areas without reticulated water, residents can maintain rainwater quality by cleaning gutters using a first flush diverter, and inspecting and cleaning the rainwater tank regularly. Generally, adults and children should not drink water or use water for cooking if it contains antimony above the ADWG of 3 micrograms/L.

If you live in an area with naturally high levels of antimony in soils and dust, the rainwater could be tested for antimony to check the levels are safe. Young children should not drink water containing detectable levels of antimony (ie 1 microgram/L). This includes water used to make children's drinks or baby formula.

Dust and soil:

You can reduce any health risk to you and your family by reducing the amount of dust and soil that you or your children swallow.  Therefore:

•	Prevent young children from swallowing soil

•	Wash your hands before eating and drinking

•	Wash young children's hands frequently

•	Wash children's toys to remove dust or soil

•	Mop dust frequently with a damp cloth.

# Is there a medical test to check for antimony?

Urine testing can be useful to check if people are currently exposed to antimony. Speak to your doctor about testing. Your doctor may also consult with clinical toxicologists at the Austin Hospital to help interpret test results.

•

Hair testing is not recommended as it can be difficult to tell the difference between antimony on the outside of the hair (from dust or water) and antimony inside the hair (taken into the body by eating or drinking).

# Where can I get more information?

Your doctor:  for advice about your personal health. Poisons Information Line 13 11 26

General information on antimony and health: Environmental Health, Department of Health 1300 761 874

Last updated: 30 May 2014.

1One microgram =1millionth of a gram

Golder Associates Pty Ltd

Building 7, Botanicca Corporate Park

570 – 588 Swan Street

Richmond, Victoria 3121

Australia

T: +61 3 8862 3500

# Text boxes

TDI 1 year old = 60 µg /day (10 kg)

TDI 2 year old = 90 µg /day (15 kg)

TDI 5 year old child = 180 µg /day

TDI 2 year old = 90 µg /day

TDI 5 year old  = 180 µg /day

TDI 1 year old = 60 µg /day

Antimony (Filtered)

Cadmium  (Filtered)

Antimony

Arsenic

Arsenic  (Filtered)

Cadmium

Copper

Copper (Filtered)

Iron

Iron (Filtered)

Lead

Lead (Filtered)

Nickel

Nickel (Filtered)

Zinc

Zinc (Filtered)

pH (Field)

pH (Lab)

Total Dissolved

Solids @180°C

Sulphate (as SO4) (Filtered)

| SDG Field_ID Sampled_Date-Time | EM1405428 EM1405428 14/5001_20140603 14/5801_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 | EM1405428 EM1405428 14/5002_20140603 14/5802_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 | EM1405428 EM1405428 3/5001_20140603 3/5801_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 | EM1405428 EM1405428 13/5001_20140603 13/5801_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 |
| --- | --- | --- | --- | --- |

| SDG | EM1405428 | EM1405428 |  | EM1405428 | EM1405428 |  |
| --- | --- | --- | --- | --- | --- | --- |
| Field_ID Sampled_Date-Time | 4/5001_20140603 3/06/2014 15:00 | 4/5801_20140603 3/06/2014 15:00 | RPD | 13/5002_20140603 3/06/2014 15:00 | 13/5802_20140603 3/06/2014 15:00 | RPD |

| SDG Field_ID Sampled_Date-Time | EM1405428 Interlab_D 3/5001_20140603 3/5901_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 | EM1405428 Interlab_D 13/5001_20140603 13/5901_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 | EM1405428 Interlab_D 14/5001_20140603 14/5901_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 | EM1405428 Interlab_D 4/5001_20140603 4/5901_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 |
| --- | --- | --- | --- | --- |

| EM1405428 EM1405428 EM1405497 EM1405497 EM1405497 EM1405428 EM1405428 EM1405428 EM1405428 EM1405428 EM1405428 EM1405497 EM1405497 EM1405428 EM1405428 EM1405428 EM1405428 EM1405428 EM1405374 EM1405374 EM1405497 EM1405497 EM1405497 EM1405562 EM1405562 EM1405497 EM1405497 EM1405428 EM1405428 EM1405428 EM1405428 EM1405497 EM1405497 EM1405374 EM1405374 EM1405428 EM1405428 EM1405428 EM1405497 EM1405497 EM1405497 EM1405428 EM1405428 EM1405428 EM1405428 EM1405428 EM1405562 EM1405562 EM1405562 EM1405562 EM1405428 EM1405428 EM1405497 EM1405497 EM1405497 EM1405497 EM1405497 EM1405497 EM1405497 EM1405562 EM1405562 EM1405562 EM1405562 EM1405562 EM1405562 EM1405562 EM1405374 EM1405374 EM1405562 EM1405562 EM1405374 EM1405374 EM1405497 EM1405497 EM1405562 EM1405562 EM1405562 EM1405497 EM1405562 EM1405497 | 5.9 6.1 5 5.3 4.5 4.6 4.8 6.6 5.5 5.3 4.6 4.7 4.7 6.2 5.4 4.4 5.4 7.3 5.3 4.5 4.8 5.2 4.5 5.6 5.2 6.6 6.9 5.5 6 7.1 5.3 7.4 6.1 6.5 4.7 5.1 5.5 6.3 5.5 6.4 5.7 5.3 6.4 6.4 5.4 4.8 4.4 4.7 4.1 4.7 4.6 4.2 4.9 4.4 5.4 6.3 6 4.5 4 6.8 5.3 4.5 5.6 3.9 5.5 5.5 6.2 5.4 4.2 5.3 4.2 6.5 6.2 5.2 5.8 4.2 6.2 6.3 7.7 7.3 | - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - 2.2 1.2 0.4 <0.1 - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - 9.2 1.8 0.6 <0.1 - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - | 9,680 6,780 | 697 126 4,230 186 | 82,500 533 34,700 189 | - - - - - - - - - - - - - - - - - - - 38 - - - - - - - - - - - - - 115 - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - | 19 - - 41.7 90 - - 38.2 428 - - 17.2 36 <50 - 26.4 14 60 - 24.3 36 - - 17.6 53 - - 20.1 1,390 - - 49.4 7 - - 15.1 16 - - 27.6 31 - - 48.7 12 - - 22.6 13 - - 29 20 - - 17.3 20 - - 8.8 24 - - 19.9 176 <50 - 14.8 376 250 - 10.2 48 - - 49.9 29 <50 46,700 23.8 14 - - 21.6 12 - - 23.6 21 - - 9 25 - - 23.9 53 - - 43.7 142 - - 15.5 44 - - 12.6 36 <50 - 37.8 114 - - 33.8 141 - - 44.7 50 - - 31.4 164 - - 29.6 41 - - 35.7 50 <50 31,800 26.5 13 - - 22.7 14 - - 27.6 58 <50 - 28.6 22 <50 - 8.3 57 - - 37 136 - - 13.5 28 - - 17 108 - - 31.9 179 <50 - 44.5 89 <50 - 15.5 24 <50 - 47.3 19 - - 33.8 16 - - 37 22 - - 28.2 30 - - 15 21 - - 16.5 10 - - 12.7 4 - - 12.9 22 - - 23.8 44 - - 18.4 104 - - 35.9 84 - - 15.4 53 - - 37.9 140 <50 - 35.7 121 <50 - 11.3 323 - - 19.3 202 - - 35.8 8 - - 22.8 19 - - 15.5 38 - - 8.2 22 - - 20.4 26 - - 36.8 60 - - 27.5 32 - - 42 43 - - 14.1 24 - - 18.2 14 - - 13.8 63 - - 20.2 55 - - 38.9 20 - - 16.9 99 - - 37.9 35 - - 10.9 38 - - 14.7 64 - - 17.4 490 - - 7.1 140 - - 9.9 |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | 10,800 126 16 59,900 76 14,300 168 22 63,700 157 22,300 <5 6 40,000 42 9,720 97 18 36,800 110 8,170 76 15 33,800 261 4,480 8 <5 7,980 714 3,900 72 9 6,590 128 7,100 592 68 19,800 132 2,640 125 <5 4,240 438 7,660 1,040 115 32,000 184 10,700 181 31 50,700 302 8,610 908 124 69,600 131 11,500 10 <5 14,600 91 11,800 <5 7 22,500 1,170 7,740 28 12 17,500 697 7,000 189 45 20,000 452 7,140 244 27 19,000 318 9,020 200 14 44,800 141 6,540 190 11 15,800 77 6,250 44 6 11,800 299 6,100 10 22 67,300 16 3,740 3,140 236 8,860 125 1,280 89 <5 3,770 351 3,770 35 23 7,340 140 5,650 116 34 32,400 380 5,060 182 16 8,260 436 4,320 26 25 37,600 1,180 13,400 114 10 21,500 610 6,870 73 19 16,100 128 5,660 50 12 13,300 298 6,780 112 33 36,700 328 5,080 20 8 11,200 306 4,850 67 11 22,100 235 6,000 613 72 27,900 264 5,490 195 20 23,500 299 7,430 10 14 31,400 100 6,100 930 106 24,000 228 3,910 600 37 10,200 323 7,310 791 79 55,500 42 4,120 331 28 25,400 197 4,450 410 21 8,640 493 7,330 2,310 367 23,600 236 2,700 11 5 3,030 95 3,540 212 13 6,810 160 4,750 92 12 24,000 77 5,090 60 7 12,300 124 8,340 104 9 32,900 42 9,330 14 8 34,300 42 9,970 18 7 31,200 304 8,690 20 8 33,200 60 3,230 9 <5 5,250 40 11,000 <5 7 18,300 72 4,110 30 5 7,510 277 4,760 16 7 9,500 157 4,730 199 9 9,140 229 3,720 51 <5 6,790 335 4,190 90 6 7,740 216 3,050 15 <5 7,450 205 3,470 80 8 17,700 183 4,570 1,920 148 30,100 86 6,360 62 18 46,500 154 6,230 <5 10 36,200 34 4,380 1,190 93 26,200 142 5,580 1,060 59 16,700 212 9,080 <5 5 15,700 1,650 4,250 10 <5 8,590 1,150 4,340 22 8 21,800 44 4,680 19 7 15,400 130 9,820 87 10 33,600 162 4,680 <5 21 12,700 162 5,710 126 22 21,500 132 9,420 389 56 48,100 119 3,100 141 10 7,420 235 2,930 <5 <5 3,250 23 2,310 3,540 68 28,700 242 6,110 14 <5 35,900 330 3,530 19 <5 33,000 304 6,770 9 15 45,900 252 |  |  |

PH_CACL2

Exchangeable Calcium

Exchangeable Magnesium

Exchangeable Potassium

Exchangeable Sodium

Aluminium

Antimony

Arsenic

Iron

Manganese

CEC

Electrical Conductivity @ 25°C

Sulphate (as SO4)

Total Organic Carbon

Moisture

PH_CACL2

Exchangeable Calcium

Exchangeable Magnesium

Exchangeable Potassium

Exchangeable Sodium

Aluminium

Antimony

Arsenic

Iron

Manganese

CEC

Electrical Conductivity @ 25°C

Sulphate (as SO4)

Total Organic Carbon

Moisture

|  | SDG Field_ID Sampled_Date-Time | EM1405428 EM1405428 14/4001_20140603 14/4801_20140603 3/06/2014 15:00 3/06/2014 15:00 | RPD | EM1405428 EM1405428 14/4002_20140603 14/4802_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 | EM1405428 EM1405428 3/4001_20140603 3/4801_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 | EM1405428 EM1405428 13/4001_20140603 13/4801_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 | EM1405428 EM1405428 4/4001_20140603 4/4801_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Chem_Group | ChemName | Units | EQL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Heavy Metals | Aluminium | mg/kg | 50 : 10 (Interlab) | 13400 | 7420 | 57 | 6870 | 7640 | 11 | 9720 | 9710 | 0 | 5060 | 5170 | 2 | 4480 | 5460 | 20 |
|  | Antimony | mg/kg | 5 : 10 (Interlab) | 114 | 120 | 5 | 73 | 83 | 13 | 97 | 58 | 50 | 182 | 155 | 16 | 8 | 8 | 0 |
|  | Arsenic | mg/kg | 5 : 2 (Interlab) | 10 | 10 | 0 | 19 | 44 | 79 | 18 | 16 | 12 | 16 | 20 | 22 | <5 | 5 | 0 |
|  | Iron | mg/kg | 50 : 5 (Interlab) | 21500 | 20600 | 4 | 16100 | 17000 | 5 | 36800 | 29400 | 22 | 8260 | 15500 | 61 | 7980 | 10700 | 29 |
|  | Manganese | mg/kg | 5 | 610 | 673 | 10 | 128 | 116 | 10 | 110 | 106 | 4 | 436 | 430 | 1 | 714 | 504 | 34 |
| Sample Quality Parameters | Electrical Conductivity @ 25°C | uS/cm | 1 : 10 (Interlab) | 141 | 127 | 10 | 50 | 66 | 28 | 36 | 38 | 5 | 36 | 37 | 3 | 1390 | 1780 | 25 |
|  | Moisture | % | 1 : 0.1 (Interlab) | 44.7 | 40.5 | 10 | 31.4 | 34.4 | 9 | 17.6 | 18.1 | 3 | 37.8 | 37.9 | 0 | 49.4 | 43.3 | 13 |
| Unknown | PH_CACL2 | pH Unit | 0.1 | 7.1 | 7 | 1 | 5.3 | 5.4 | 2 | 4.6 | 4.7 | 2 | 5.5 | 5.5 | 0 | 6.6 | 6.4 | 3 |

|  | SDG Field_ID Sampled_Date-Time | EM1405428 Interlab_D 3/4001_20140603 3/4901_20140603 3/06/2014 15:00 3/06/2014 15:00 | RPD | EM1405428 Interlab_D 13/4001_20140603 13/4901_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 | EM1405428 Interlab_D 4/4001_20140603 4/4901_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 | EM1405428 Interlab_D 14/4001_20140603 14/4901_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 | EM1405428 Interlab_D 14/4002_20140603 14/4902_20140603 RPD 3/06/2014 15:00 3/06/2014 15:00 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Chem_Group | ChemName | Units | EQL |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Heavy Metals | Aluminium | mg/kg | 50 : 10 (Interlab) | 9720 | 11000 | 12 | 5060 | 3900 | 26 | 4480 | 7100 | 45 | 13400 |  |  | 6870 | 9100 | 28 |
|  | Antimony | mg/kg | 5 : 10 (Interlab) | 97 | 120 | 21 | 182 | 210 | 14 | 8 | 11 | 32 | 114 |  |  | 73 | 110 | 40 |
|  | Arsenic | mg/kg | 5 : 2 (Interlab) | 18 | 4.7 | 117 | 16 | 8.9 | 57 | <5 | 4 | 22 | 10 |  |  | 19 | 18 | 5 |
|  | Iron | mg/kg | 50 : 5 (Interlab) | 36800 | 45000 | 20 | 8260 | 10000 | 19 | 7980 | 11000 | 32 | 21500 |  |  | 16100 | 21000 | 26 |
|  | Manganese | mg/kg | 5 | 110 | 80 | 32 | 436 | 490 | 12 | 714 | 630 | 13 | 610 |  |  | 128 | 110 | 15 |
| Sample Quality Parameters | Electrical Conductivity @ 25°C | uS/cm | 1 : 10 (Interlab) | 36 | 41 | 13 | 36 | 61 | 52 | 1390 | 940 | 39 | 141 |  |  | 50 | 54 | 8 |
|  | Moisture | % | 1 : 0.1 (Interlab) | 17.6 | 17 | 3 | 37.8 | 41 | 8 | 49.4 | 49 | 1 | 44.7 | 41 | 9 | 31.4 | 34 | 8 |
| Unknown | PH_CACL2 | pH Unit | 0.1 | 4.6 |  |  | 5.5 |  |  | 6.6 |  |  | 7.1 |  |  | 5.3 |  |  |

| SDG | EM1405428 | Interlab_D |  |
| --- | --- | --- | --- |
| Field_ID Sampled_Date-Time | 26/4001_20140603 3/06/2014 15:00 | 26/4901_20140603 3/06/2014 15:00 | RPD |

3

| Sample Number | 14-449 | 14-450 | 14-451 |
| --- | --- | --- | --- |
| Start Date/TimeA | 4/06/2014 00:00 | 6/06/2014 00:00 | 8/06/2014 0:00 |
| End Date/TimeA | 4/06/2014 16:48 | 7/06/2014 0:00 | 9/06/2014 0:00 |
| Sample Period | 16.8 hoursB | 24 hours | 24 hours |
| Size Selective Inlet Manufacturer and Model | PM10 Ecotech | PM10 Ecotech | PM10 Ecotech |

| Sample Number | 14-444 | 14-445 | 14-446 |
| --- | --- | --- | --- |
| Start Date/TimeA | 4/06/2014 00:00 | 6/06/2014 00:00 | 8/06/2014 0:00 |
| End Date/TimeA | 4/06/2014 16:48 | 7/06/2014 0:00 | 9/06/2014 0:00 |
| Sample Period | 16.8B | 24 hours | 24 hours |
| Size Selective Inlet Manufacturer and Model | PM2.5 Ecotech | PM2.5 Ecotech | PM2.5 Ecotech |

PM10 Concentration (µg/m3)

3 Jun 13:15

4 Jun 13:15

5 Jun 13:15

6 Jun 13:15

7 Jun 13:15

8 Jun 13:15

9 Jun 13:15

10 Jun 13:15